## Slide 1: GCC ASCEND 2
Low Cost of Entry Wireless Mobile Network

## Slide 2: Abstract
Assemble and configure system featuring Embedded System, GPS, Altimeter, and Radio
Demonstrate the employability of supplemental networking by streaming live video
Develop and configure necessary topology for fully functional WMN;
Correct and Improve PtP system for future PtMP employment
Evaluate shortcomings of COTS comp. inclusions
Non-Deterministic Team Management

## Slide 3: Proof of Concept
Wireless Communication over 900mhz
Limitations: Resources, Crowded Signal, TX/RX Power
Elected New Frequency of 12cm band (2.4 ghz)
New Hardware & Development Platform
Shift in Application Target Employment;
  Transmission of sensor data gauged wireless connectivity
  Availability of tech afforded opportunity to push ASCEND program limits

## Slide 4: Revisions
New Development Platform:
  SolidRun Hummingboard i2ex Donated, Supported
  i.MX6 Dual Processor
  1080P GPU Level Capability
  MIPI CSI 2.0, 2 Lane CSI-2 Camera Interface
  PCIe Gen II
  Android KitKat & Linux Distro
  Neo 6M GPS Module
  Buck-booster integrated into necessary POE Radio

## Slide 5: Objective
An effective and sufficiently functioning payload for PtP Near-Space Telecommunications
Streaming real-time >=460p @ 14fps video to demonstrate quality of signal; reduce system complexity and scope to fundamental
Implement Differential GPS to serve as reference frame for tracking; auto-configuring station TX/RX

## Slide 6: Intent
Intended market, potential applications
Affordable mobile network solutions for wide ranging employment such as:
  Disaster Relief
  Developing Infrastructure
  Remote/Rescue Operations
  Supplementary Secured Network for Defensive Applications

## Slide 7: System Overview
Ubiquiti Bullet-M Radio Specifically Designed for Long-Range PtP Networking
Carrier Class Throughput Up to 100Mbps Within 50km Range
24v 0.5a PoE Source
Cat-6 Ethernet Between i2ex & Bullet
Rocket M2 Base Station With NanoBridge Directional

## Slide 8: Telecommunications
Payload tx power requires highly accurate directional
Requirements/Limitations necessitate accuracy
Differential GPS increases tracking resolution, auto-configures based on signal strength
Free Space Loss(12cm band) over ~35km:
Loss(21mi)=20log(2400mhz)+20log(21mi)+36.6 ~130.2dB
Loss(25mi) ~132.2dB

## Slide 9: Telemetry
DoD limitations limit GPS positional location by way of timing errors; generally under 20 meters
DGPS can correct, improve accuracy from (2cm., 2m)
Neo-6M GPS HW access allowed RAW data access
Assuming errors of proximity were within relative range of each other
*****ADSDDDDSA*****

## Slide 10
SolidRun i2ex Hummingboard

## Slide 11: Ubiquiti Bullet-M/NanoBridge

## Slide 12: System Graphically

## Slide 13: Software Abstract
Capture full HD video
Stream real-time video and data to local network
Host server to capture data, present in usable format.

## Slide 14: Software
First approaches
  Difficulties
    Stable environment
    Android rapid development support
  Solutions
    Changed development location.
    Changed systems

## Slide 15: Software Technicals
Debian Jessie
  Mostly supported but out of date kernel
Debian Wheezy
  Many out of the box solutions.
  Large support community
  Camera – Initial attempts and final solution
  GPS – Ease of use

## Slide 16: Wireless Network Setup
One Ubiquiti Bullet connected to a Hummingboard-i2ex
One Ubiquiti NanoBeam connected to a laptop
Both devices set up as a wireless bridge
Initial testing was done across 10 meters

## Slide 17: Barometer
BMP180 pressure/temperature sensor
Communicating to the Hummingboard via I2C
Using SMBus protocol
Library programmed in Python using the python-smbus module
Temperature testing done using a digital thermometer
Pressure testing done using the elevation of the nearest weather station

## Slide 18: Assembly
Adhering to weight limitations
Structural integrity
Mechanically fastening components
System assembly as a whole

## Slide 19: Antenna Specifications

## Slide 20
Antenna Specifications

## Slide 21
Antenna Specifications

## Slide 22
Antenna Specifications

## Slide 25: Mapping
Ground Directional LOS Precision
Using GPS Coordinates with Numerical Method/Vector Auto Regression to Best “follow” Payload
Accuracy Allows Weak Omni-Directional to Transmit

## Slide 26: Frame Transfer

## Slide 27: Desired Relation

## Slide 28: Struggles
Time & Resources
Weight Limitations / Available Power
Necessary Proficiency with Android API
Geodesic Telemetry and Triangulation
Numerical Methods/Complex Analysis for Mapping

## Slide 29: Results
Fall 2014
Power
Raw Data
  6 miles
  Resets
Antenna Usage
Launch Sequence
Spring 2015
Power challenges
Data Prospects
  10 miles HD images
  Component Stability
Antenna Usage
Launch Sequence

## Slide 30: Residuals
Overview of Rudimentary System and Resulting Depth
Multidisciplinary Unification & Necessary Proficiency Beyond Subject Area
Team Dynamics & Progressive Methods for Non-Deterministic Short-Run Development
Continuation of Research Into Graduate Level

## Slide 31: Residuals