## Slide 1: Power System
David Riddle

## Slide 2: Overview
Power Board
Energy Budget of ERAU Eagle Satellite
TASC Solar Panel Test
TrisolX Soler Cells

## Slide 3: Power Board
TrisolX solar cells to charge an Array of Super Capacitor
Charge and discharge faster than most rechargeable batteries
Have more charge and discharge cycles
Larger than equivalent battery

## Slide 4: Super Capacitors
Eaton Bussmann HV1030-2R7106-R
Capacitance of 10F
Voltage rating of 2.7V
Operating Temp range
  -40 to 65 °C
Radial leads

## Slide 5: Super Capacitor Array

## Slide 6: Energy Budget
Component | Voltage (V) | Current (mA) | Power (mW) | Duty Cycle (%) | Orbit (min) | Eff. (%) | Dis. Energy (J) | Charge Energy (J)
PV Panel |  |  | 1300 | 100 | 60 | 60 |  | 2808
EPS |  |  | 156 | 100 | 60 | 80 | -561.6 | 
OBC | 3.3 | 20 | 66 | 100 | 60 |  | -237.6 | 
OBC (Eclipse) | 3.3 | 1 | 3.3 | 100 | 20 |  | -3.96 | 
Receiver | 7.2 | 45 | 324 | 100 | 60 |  | -1166.4 | 
Transmitter | 7.2 | 290 | 2088 | 5 | 60 |  | -375.84 | 
GPS Ant | 3.3 | 30 | 99 | 10 | 60 |  | -35.64 | 
GPS | 3.3 | 303.03 | 1000 | 10 | 60 |  | -360 | 
Memory | 3.3 | 20 | 66 | 10 | 60 |  | -23.76 | 
Total |  |  |  |  |  |  | -2764.8 | 2808

## Slide 7: Solar Panel Test
40 Watt Tungsten Light Bulb
Using the Top Solar Panel with GPS hole
21 TASC Solar Cells

## Slide 8: TASC Solar Cell
Triple-junction gallium arsenide
Area 2.277 cm2 (0.353 sq. in.)
Isc= 31 mA
Imp= 28 mA
Voc= 2.52 V
Vmp= 2.19 V
Pmp= 0.027 W/cm2
Cff= 80 %
Efficiency= 27 ± 3% Absolute
Temp. Coeff. Vmp = -6.2 mV/°C

## Slide 9: Solar Panel

## Slide 10: Solar Panel Test

## Slide 11: TrisolX Solar Cells
Triple-junction gallium arsenide
Area 1.3 cm2 (0.353 sq. in.)
Imp= 14.6 mA
Voc= 2.62 V
Vmp= 2.33 V
Pmp= 34 mW
Efficiency= 28 %
Temp. Coeff. Vmp = -6.1 mV/°C

## Slide 12: Questions