## Slide 1: Improving the Reliability of GPS Tracking Beacons
Clayton Jacobs
jacobsc6@my.erau.edu
Mentor: Jack Crabtree

## Slide 2: Outline
Program History
Legacy Designs
New Hardware Specifications
Design Methodology
System Description
Future Developments

## Slide 3: Program History
Embry-Riddle Project HiBall created to support the launch of high altitude balloons from ERAU campus.
Balloon train consists of multiple payloads which support on-campus organizations
  Engineering Classes: AE226, Experimental Space Systems Lab
  Preliminary/Detain Design: AE427
  NASA ASCEND!
  ERAU Summer Camps: Middle/High School Students
Beacons support the launch, ascent, decent and recovery
  Provide position and velocity information on the airborne balloon

## Slide 4: Legacy Designs

## Slide 5: Legacy Designs
Sample Post-Flight Data (ANSR-88)

## Slide 6: Legacy Designs
Maintainability
  N7ERU beacons rebuilt before each flight and tested for correct operation. Damage from previous flights was corrected by short-term fix or replacement
Flaws
  Heavy: Over 2lbs
  Reprogramed before flight
  High failure rate, unknown causes
    Long wires, RF interference, unseen damage

## Slide 7: New Hardware Specifications
Total weight under 2lbs
  Minimize weight
24 Hour battery life
  Maximize operational time
Beacon must be reusable
  Ability to perform maintenance is important
  Must be reprogrammed for each flight

## Slide 8: Design Methodology
Byonics TinyTrak3plus (TT3+)
  Converts serial GPS data into analog audio tones to be transmitted by the transceiver
  Converts the GPS information into a standard APRS packet structure for reception by Amateur Radio operators
Venus GPS
  Reports serial NMEA formatted position/velocity information
  Not limited to 60,000ft AGL
UHF Transceiver SA828
  Transmits analog audio signals as RF
  Operating range from 400Mhz-480Mhz

## Slide 9: System Block Diagram
Support Circuitry
TT3+
Venus GPS
UHF
TCVR
Audio Signal
Signal Ground
Serial Receive
Serial Transmit
12V Battery
3.3V Regulator
5.0V Regulator

## Slide 10: Further Development
Assemble functional circuit board when the PCB is delivered.
Test system performance under thermal and pressure cycling in a thermal vacuum chamber with the addition of RF interference.
First scheduled flight in June 2015 on ERAU Summer Camp balloon.
Write a user guide which includes:
  Circuit Descriptions
  Maintenance procedures
  Operation procedures

## Slide 11: Acknowledgements
Dr. Gary Yale –ERAU Space Grant Coordinator
Prof. Jack Crabtree – Project Mentor

## Slide 12: End
Thank you for your attention.