## Slide 1: Microfluidic system for label-free chemical/biological detection using nanowire FET sensors
Christy Contreras
Physics Department, Arizona State University

## Slide 2: Motivation: Personalized Medicine

## Slide 3: Motivation: Personalized Medicine

## Slide 4: Motivation: Personalized Medicine

## Slide 5: Proposed Solution: An Integrated System
Innovative and powerful integrated technology

## Slide 6: Proposed Solution: An Integrated System
Innovative and powerful integrated technology
Able to handle small liquids and detect biomolecules like protein and DNA

## Slide 7: Proposed Solution: An Integrated System
Innovative and powerful integrated technology
Able to handle small liquids and detect biomolecules like protein and DNA
Revolutionary tool for biomedical applications and disease diagnostics

## Slide 8: Proposed Solution: An Integrated System
Innovative and powerful integrated technology
Able to handle small liquids and detect biomolecules like protein and DNA
Revolutionary tool for biomedical applications and disease diagnostics
Two components: an FET biosensor and a microfluidic platform

## Slide 9: What are FET biosensors and how do they work?
Gate 2
Gate 1
Source
Drain
40um
Dimensions: Silicon nanowire 30 nm in diameter, gate gap distance is 2 um

## Slide 10: What are FET biosensors and how do they work?
Source and drain electrodes
Gate electrode pair
Silicon nanowire
Gate 2
Gate 1
Source
Drain
40um
Dimensions: Silicon nanowire 30 nm in diameter, gate gap distance is 2 um

## Slide 11: What are FET biosensors and how do they work?
Source and drain electrodes
Gate electrode pair
Silicon nanowire
Antibody modification of electrode gates
Gate electrode pair
Silicon
nanowire
Gate 2
Gate 1
Source
Drain
40um
Dimensions: Silicon nanowire 30 nm in diameter, gate gap distance is 2 um

## Slide 12: What are FET biosensors and how do they work?
Source and drain electrodes
Gate electrode pair
Silicon nanowire
Antigen recognition and binding events occur
Antibody modification of electrode gates
Gate electrode pair
Silicon
nanowire
Gate 2
Gate 1
Source
Drain
40um
Dimensions: Silicon nanowire 30 nm in diameter, gate gap distance is 2 um
Antibody
modification

## Slide 13: What are FET biosensors and how do they work?
Source and drain electrodes
Gate electrode pair
Silicon nanowire
Antigen recognition and binding events occur
Antibody modification of electrode gates
Signal change occurs when antigen flow is introduced
Gate electrode pair
Silicon
nanowire
Gate 2
Gate 1
Source
Drain
40um
Dimensions: Silicon nanowire 30 nm in diameter, gate gap distance is 2 um

## Slide 14: What is a microfluidic system and why is it useful?
Microfluidics is a network of micro-sized channels that handle small fluid samples
Inlets
Outlet
Micro-channels

## Slide 15: What is a microfluidic system and why is it useful?
Microfluidics is a network of micro-sized channels that handle small fluid samples
Used to mix, sort, and transfer fluids
Inlets
Outlet
Micro-channels

## Slide 16: What is a microfluidic system and why is it useful?
Microfluidics is a network of micro-sized channels that handle small fluid samples
Used to mix, sort, and transfer fluids
Come in various arrays of patterns and designs depending on the purpose
Inlets
Outlet
Micro-channels

## Slide 17: What is a microfluidic system and why is it useful?
Microfluidics is a network of micro-sized channels that handle small fluid samples
Used to mix, sort, and transfer fluids
Come in various arrays of patterns and designs depending on the purpose
Properties:
Inlets
Outlet
Micro-channels

## Slide 18: What is a microfluidic system and why is it useful?
Microfluidics is a network of micro-sized channels that handle small fluid samples
Used to mix, sort, and transfer fluids
Come in various arrays of patterns and designs depending on the purpose
Properties:
  Inexpensive and compact
Inlets
Outlet
Micro-channels

## Slide 19: What is a microfluidic system and why is it useful?
Microfluidics is a network of micro-sized channels that handle small fluid samples
Used to mix, sort, and transfer fluids
Come in various arrays of patterns and designs depending on the purpose
Properties:
  Inexpensive and compact
  Multiple inputs
Inlets
Outlet
Micro-channels

## Slide 20: What is a microfluidic system and why is it useful?
Microfluidics is a network of micro-sized channels that handle small fluid samples
Used to mix, sort, and transfer fluids
Come in various arrays of patterns and designs depending on the purpose
Properties:
  Inexpensive and compact
  Multiple inputs
  Laminar flow (diffusion mixing)
Inlets
Outlet
Micro-channels

## Slide 21: Microfluidic System Demonstration
Channel width: 50um, 100um, 200um

## Slide 22: Microfluidic System Demonstration
Channel width: 50um, 100um, 200um

## Slide 23: Microfluidic Chip Fabrication
1
SU-8
Coat with SU-8

## Slide 24: Microfluidic Chip Fabrication
UV exposure
2
1
SU-8
Coat with SU-8
Place mask & expose

## Slide 25: Microfluidic Chip Fabrication
UV exposure
2
1
3
SU-8
Coat with SU-8
Place mask & expose
Wash away SU-8 and cure

## Slide 26: Microfluidic Chip Fabrication
UV exposure
2
1
3
4
SU-8
Pour PDMS
Coat with SU-8
Place mask & expose
Wash away SU-8 and cure

## Slide 27: Microfluidic Chip Fabrication
UV exposure
2
1
3
5
4
SU-8
Peel off mold
Pour PDMS
Coat with SU-8
Place mask & expose
Wash away SU-8 and cure

## Slide 28: Microfluidic Chip Fabrication
UV exposure
2
1
3
5
4
6
SU-8
Peel off mold
Pour PDMS
Bond to glass slide
Coat with SU-8
Place mask & expose
Wash away SU-8 and cure

## Slide 29: Experiment Setup
Syringe Pump
Microfluidic chip
Syringe
Food Coloring
Tubing
Microscope

## Slide 30: Summary of Results
We were able to fabricate a microfluidic device and show the laminar flow occurring, but we saw that diffusion did not occur inside the channel. We want calculate how long the channel must be in order for diffusion mixing of liquids to occur.

## Slide 31: Future Experiments
Currently we are testing the alignment and bonding of a simple microfluidic device on the nanowire FET.
Upcoming work:
We eventually want to run some pH sensing tests on the nanowire FET biosensor. Later we will do protein recognition tests.

## Slide 32: Acknowledgements
Research mentor: Dr. Quan Qing
Lab partners: Yuan Wang, Xiangbing Liao, Joshua Sadar
Research Funding: ASU/NASA Space Grant

## Slide 33: Thank you for your attention! Any Questions?
Christy Contreras
ccontr11@asu.edu