## Slide 1: Implantable Bone Sensors for Monitoring Fracture Healing
Leonel Almanzar
Dr. David Margolis
University of Arizona: Orthopedic Surgery
AZ Space Grant Symposium 2024

## Slide 2: Statement of Problem
Bones need weight to be healthy
Astronauts loose bone mass due to to microgravity
We need a method to monitor bone health in space
Implantable sensors we are currently using to measure fracture healing may be useful to monitor bone health in space

## Slide 3: Objectives
Implant Osseo surface (bone surface) sensors onto fractured sheep femur
Measure and collect the strain and load the sheep place on their femur
Analyze the strain over time to see fracture healing

## Slide 4: Methods
1. Set up the wireless telemetry system
2. Measure the strain data while walking on treadmill
3. Measure the strain and load as the sheep rocks
4. Use the strain and load data to find the stress

## Slide 5: Wireless Telemetry Setup
Sensor is powered using magnetic resonance
Data is collected using near-field communication (NFC) with the antennas
Continuously scans for the data on the sensor
Figure 1: photograph of the Osseo surface sensor
Figure 2: Functional block diagram of sensor

## Slide 6: Walking
Sheep walks on treadmill for around 1-2 min
Measure the strain on the bone
Select correct data using video and graphs
Figure 3: Video of sheep walking on treadmill and
Figure 4: Strain vs time graph showing walking pattern

## Slide 7: Rocking
Rock the sheep back and forth
Measure how much strain and load
Using time and video to accurately align the load and strain data
Figure 5: Video of sheep rocking while collecting load and strain

## Slide 8: Results
Figure 6: Average Peak to Peak Strain between Week 5 and Week 12

## Slide 9: Results
Week 5
Week 6
Week 7
Week 8
Week 10
Week 11
Week 12
*
*
*
*
*
*
*
Figure 8: X-ray images between Week 5 to Week 12

## Slide 10: Interpretation
For the first five weeks, the strain decrease
After Week 10, the strain goes up
From our initial testing, the sensors are showing good data

## Slide 11: Impact
Continuing to improve the use of these sensors will be critical for astronauts in space
Analyzing strain and stress with other data will clearly show bone health and density
Hopefully, one day these sensors will be in space

## Slide 12: Acknowledgements
PI: Dr. David Margolis
Space Grant Manager: Michelle Coe
Lab Manager: David Gonzales
PhD Student: Gerardo Figueroa

## Slide 13: Thank You