## Slide 1: CatSat: Preparing for CubeSat Flight Operations and Science
Walter Rahmer
Dr. Christopher Walker, Steward Observatory, University of Arizona
University of Arizona
20 April 2024

## Slide 2: Overview
6U CubeSat built by the University of Arizona
~30 x 20 x 10 centimeter box
Onboard:
High Frequency Experiment
Inflatable Antenna Technology Demonstration
HD Camera
HAM Radio Repeater

## Slide 3
CAD Model of CatSat Deployed in Space.
Image Credit: Aman Chandra, FreeFall Aerospace

## Slide 4: My Work
HD Camera – Aperture Correction
Magnetometer – Calibration and testing
AstroSDR – Data capture troubleshooting
Metrology Cameras – Focus Setting
Ground Station – Low Noise Amplifier Installation
Data Processing – Xmidas packet interpretation
Full Spacecraft – Final Assembly
+ More

## Slide 5: The HF Experiment
The ionosphere is a layer of charged particles in the upper atmosphere that interferes with radio signals, especially around the High Frequency (HF) band.
Understanding this effect is necessary for all radio communication that interacts with the ionosphere (e.g. GPS signals, short wave radio communication).
The ionosphere is significantly different between day and night, and the transition period is chaotic

## Slide 6: The HF Experiment
2-foot whip antenna deployed from the bottom of CatSat
Listen for known HF signals such as WWV or HAM radio WSPR signals
Compare received signals to known transmission format
Image credit: Dr. Christopher Walker

## Slide 7: My Work on the HF/WSPR Experiment
Problem:
Powering on the HF board draws an extreme spike of current from the batteries, tripping a fuse and restarting the entire system
Solution:
Design and construct a current limiting board to absorb the current spike and prevent it from affecting the batteries
Multiple board designs were tested and iterated over to produce a final design

## Slide 8: My Work on the HF/WSPR Experiment

## Slide 9: The Inflatable Antenna
SmallSats suffer from size and mass constraints, limiting antenna size and speed
CatSat will demonstrate an inflatable spherical antenna design to allow high speed communication
50 Mbps speeds are expected from the 0.5-meter antenna
Image Credit: Aman Chandra

## Slide 11: Balancing Needs
Pointing: How do we ensure the solar panels face the sun, while also minimizing drag and ensuring proper data collection?
Data: How much data is produced and how much can we transmit over an orbit?
Time: How do we best allocate time during an orbit? During a pass? How do we work around our classes?

## Slide 12: Summary
CatSat will demonstrate high speed communication for small satellites and collect valuable data on the Ionosphere.
My work on CatSat has spanned all its systems, fixing issues, learning procedures, and physically constructing designs.
Work continues on flight software and ground communications
CatSat passed vibrational testing last November and is ready for launch.

## Slide 13: Summary
CatSat will demonstrate high speed communication for small satellites and collect valuable data on the Ionosphere.
The program has provided invaluable experience for the students working on it.
CatSat is ready for launch soon.

## Slide 14: Acknowledgements
Dr. Christopher Walker and the incredible CatSat team
The University of Arizona
Freefall Aerospace
Rincon Research Corporation
NASA CubeSat Launch Initiative
Firefly Aerospace
NASA Arizona Space Grant
Image Credit: UA Communications

## Slide 15
Thank You