## Slide 1
Rachel Rhomberg
NASA Space Grant Undergraduate Research Symposium
April 20, 2024
Pneumatic System Integration in Supersonic Flow
Mentor: Dr. James Threadgill
Department of Aerospace and Mechanical Engineering
Special Acknowledgments:
The University Consortium for Applied Hypersonics
Arizona Research Center for Hypersonics

## Slide 2: Arizona Polysonic Wind Tunnel
Blowdown Wind Tunnel located at the AME building at UArizona
Test Section: 15in x 15in x 50in
Current Mach Range: 1.7 - 4
Run Time: 10-25 seconds
The Arizona Polysonic Wind Tunnel
Notes: Focus on understanding the effects of sweep, which requires full understanding of the unswept interaction as a baseline.

## Slide 3: Project Overview / Motivation
Jets allow for increased control of aerodynamic vehicles
The goal is to test varying jets to increase understanding of flow behavior, thus expanding our knowledge of aerodynamic control.
Notes: Focus on understanding the effects of sweep, which requires full understanding of the unswept interaction as a baseline.

## Slide 4: Jet/Model Design
Mass flow calculations helped determine proper tubing selection and nozzle design
Design Constraints
  Jet Sizes
  Tubing interface
  Manufacturability
  Structural Integrity
Notes: Focus on understanding the effects of sweep, which requires full understanding of the unswept interaction as a baseline.

## Slide 5: Velocity Profile Testing
Pressure transducer measurements were taken to test jet velocity.
Schlieren visualization was used to analyze the flow patterns surrounding the the jets, assuring a uniform flow profile at the jet exit.
Nozzle Block:
Notes: Focus on understanding the effects of sweep, which requires full understanding of the unswept interaction as a baseline.

## Slide 6: Transverse Jet in Supersonic Crossflow
Shock waves form due the freestream/jet interaction.
Separation takes place in the boundary layer.
A Prandtl–Meyer expansion fan forms, and the flow is compressed by the barrel shock wave and Mach disk.
A recompression shock wave occurs in the recirculation zone.
Notes: Focus on understanding the effects of sweep, which requires full understanding of the unswept interaction as a baseline.

## Slide 7: Future Work and Testing Plans
Further testing will provide insight into flow dynamics for optimizing pneumatic systems in supersonic environments, contributing to the advancement of aerospace technology.
Acknowledgments
UArizona-NASA Space Grant
University Consortium for Applied Hypersonics
Arizona Research Center for Hypersonics
RTX
Dr. James Threadgill
Dr. Ashish Singh
Dr. Jesse Little
Nicholas Mammana
Notes: Focus on understanding the effects of sweep, which requires full understanding of the unswept interaction as a baseline.

## Slide 8
Thank you!