## Slide 1
Trajectory Optimization for Shuttle Via Earth-Mars Cycler
Kyle Newlin, College of Engineering
Dr. Davide Conte, Dept. of Aerospace Engineering
2024 Arizona Space Grant Symposium
Tucson, AZ

## Slide 2
Cyclers are trajectories that in ideal conditions would allow a spacecraft to continually revisit two different planets, requiring just one significant burn.
This project aims to produce a MATLAB algorithm capable of optimizing and tailoring Earth-Mars cyclers to future interplanetary mission requirements.
Intro / Objective

## Slide 3
Δ
Φ
Trajectory Plane
Reference Vector
3D Flyby Targeting Circle:
where
RSOI
where TOF = tf - t0
r1
r2
Problem Parameterization
Lambert's Problem:
V∞
Δθ
t0
tf
TOF

## Slide 4
3D Flybys
Earth Flyby (Varied Orientation):
Earth Flyby (Varied Perigee):

## Slide 5
Particle Swarm Optimization
PSO: find X,Y for minimal Z
Objective Function Z = X2 + Y2

## Slide 6
Particle Elements:
X = [ JDlaunch, --, -- , TOFM1, ΔM1, ΦM1, TOFE1 … (Free Return: 5D)
ΔE1, ΦE1, TOFM2, ΔM2, ΦM2, TOFE2 … (2 Round Trips: 11D)
ΔE2, ΦE2, TOFM3, ΔM3, ΦM3, TOFE3 ] … (3 Round Trips: 17D)
… (n Round Trips: 5+6n D)
Objective Function:
Z = ΔVi + ΔVm(2 x n)
(Initial and Continual Maintenance Burns)
ΔV’s Evaluated through Lambert's Problem And Planetary Positions/Velocity Provided by NASA JPL Horizons
ΔVi
ΔVm
PSO Applied to Cyclers
V∞-
V∞+
V∞+

## Slide 7
Earth-Mars Cycler (Inbound)

## Slide 8
Results and Interpretations
Launch Date | Inbound: 16-Feb-2033 Outbound: 17-Dec-2033
Avg. TOF (Inbound Transfer) | 139 days
Avg. TOF (Outbound Transfer) | 636 days
Avg. TOF (Per Round Trip) | 775 days
Initial ΔV | 5.12 km/s
Avg. Maintenance ΔV (Per Round Trip) | 0.23 km/s