## Slide 1: Development of an Assistive Exoskeleton for a Space Suit
Dom Belasquez
Mentor: Dr. Reza Sharif Razavian
Additional Acknowledgement: Jose Ben
NAU Steve Sanghi College of Engineering
NAU Department of Astronomy and Planetary Science

## Slide 2: Introduction
2 of 16

## Slide 3: The Extravehicular Activity (EVA) Mission
Long Duration: ~7 hours [1]
NASA’s Primary EVA Space Suit: Extravehicular Mobility Unit (EMU)
Heavy: ~114 kg (No User) [1]
Bulky: 14 material layers [1]
Figure 1: EMU Diagram. Adapted from [2]
3 of 16
[1] NASA, “The Space Shuttle Extravehicular Mobility Unit (EMU),” in Suited for Spacewalking: A Teacher’s Guide with Activities for Technology Education, Mathematics, and Science, DC: Office of Human Resources and Education, 1998, pp. 17-30. [E-Book]
[2] NASA, “The Extravehicular Mobility Unit (EMU),” National Aeronautics and Space Administration. https://www.nasa.gov/image-article/extravehicular-mobility-unit-emu/

## Slide 4: Problem Definition
4 of 16
[3] J. Dunn, E. Benson, J. Norcross, and N. Newby, “Evidence Report: Risk of Injury and Compromised Performance Due to EVA Operations,” NASA, 2022.
Problem
More difficult motion in EMU suit [3]
Extra Energy Expenditure
Sweat and Moisture Buildup
Discomfort, Excessive Sweat, Skin Irritation, Fatigue [3]
Solution
Reduce Energy
Reduce Fatigue
Assistive Power Exoskeleton

## Slide 5: Power Exoskeleton Challenges
5 of 16
[4] Sarcos Robotics, “Robots: Guardian XO,” IEEE, 2020. https://robotsguide.com/robots/guardianxo
Figure 2: Sarcos Robotics Guardian XO Industrial Exoskeleton. Adapted from [4]
Bulky
Heavy: 114 kg [4]
Powerful: Lifts 850+ N [4]
EMU suit is already big and heavy: Integrating a large power exoskeleton would worsen the problem
Exoskeleton Needs: Lightweight, low volume, assistive power delivery

## Slide 6: Research Question
Can a lightweight and low volume exoskeleton assist in reducing user effort?
6 of 16

## Slide 7: The Design
Elbow (Single Joint) Actuation Focus: 1 degree of freedom
Motor: Stepper motor
Cable Driven: Bowden cable
3D Printed PLA
Lightweight: <3 kg
Low Volume: ~1.14 x 10-3 m3
Figure 3: CAD (SolidWorks) Model
7 of 16

## Slide 8: Experimental Setup
  Controller: Manual control with Arduino Uno using 2 buttons
  Power Delivery: Workbench power supply (24V @ 2.3A)
  Experiments Ran:
  Actuation while not worn
  Actuation while worn
  Actuation while worn + held mass
Figure 4: Experiment Wiring Diagram
8 of 16

## Slide 9: Testing and Results
9 of 16

## Slide 10: Experiment: Actuation While Not Worn
10 of 16

## Slide 11: Experiment: Actuation While Worn
11 of 16

## Slide 12: Experiment: Actuation While Worn + Held Mass
12 of 16

## Slide 13: Results
Conclusion: This mechanism for power actuation from a small, lightweight forearm exoskeleton can assist a user in movement!
13 of 16
    Max Lift Test: 10 N
Reliable: Lifted relaxed arm with miminal slippage
Smooth operation: Motion felt natural
Positive Outcomes
      Difficult to Apply Preload Tension: Slipped under heavier loading
      Uncomfortable: Not tailored correctly to arm
      Cable Routing Issue: Cables began to overlap and lose preload tension
Limitations
Figure 5: Cable Overlap on Motor Pulley
Notes: Don’t say water bottle, add animations, increase graphics, give design reasons for positives and negatives, just say handheld mass

## Slide 14: Future Considerations
14 of 16

## Slide 15: Future Work
Prototype Improvements
Increase Comfort: Increase brace flexibility and adjustability
Improve Tensioning Mechanism and Cable Routing
Increase Material Strength: Possible composite use
Increase Cable Strength: Cable strength close to 10 N load tension [4]
15 of 16
Design Additions
Integration with EMU Suit
Make Exoskeleton Battery Powered
Integrate Haptic Feedback
Make Backward’s Drivable
[4] TECNI, “Stainless Steel Cable 7x7 (Flexible),” TECHNI Ltd, Tech. Rep. CABLE-GP-SS-77, 2020.

## Slide 16: Thank you!
Questions?
16 of 16
Dr. Reza Sharif Razavian
Jose Ben
Dom Belasquez
Notes: Picture of Jose, Reza, Thank Space Grant Consortium for funding and opportunity