## Slide 1: Developing Novel Optical Imaging Techniques for Early Detection of Gastrointestinal Cancers
Arizona NASA Space Grant Symposium | 2025.04.19 | Supriya Roy
Advisors: Dr. Travis Sawyer and Justina Bonaventura

## Slide 2: Introduction
In detecting cancer, the state of disease is determined by a removing a sample of tissue from the patient
The sample is processed, stained, and sliced and sent to a histopathologist, who then identifies the disease state of the tissue
Generally, this process requires invasive procedures and is inefficient
  The time and cost of trainings clinicians to perform this work, the time and cost of processing the sample, and the environmental effects of staining motivate the need for other modes of clinical diagnosis
Image 1 Credit: Justina Bonaventura
Image 2 Credit: Banner University Medical Center, Imaged by Justina Bonaventura

## Slide 3: Primary Aim
In developing less invasive procedures for the early detection of cancer, the use of emerging optical technologies can optimize the efficiency and effectiveness of clinical diagnosis
Structural properties of tissue samples can be used to identify tissue disease states
My work aims to establish a method of tissue optical signature characterization by
  1. Generating a dataset of tissue images (from Banner University Medical Center) of pancreatic tissue images using multiphoton microscopy
  2. Visualizing and characterizing structural differences in normal and pathological tissue samples
  3. Finally implementing this into an AI algorithm
Image Credit: National Cancer Institute, USA. Esophageal Cancer Treatment (PDQ) https://www.cancer.gov/

## Slide 4: Generating the Tissue Sample Dataset
Normal Tissue
Tumor Tissue
Diagram Credit: BOOM Lab
Image Credit: Noelle Daigle

## Slide 5: Understanding Structural Differences
Normal Tissue
Tumor Tissue

## Slide 6: Characterizing Image Texture
Normal Tissue
Tumor Tissue
By quantizing the visual features of the tissue images using a set of mathematical equations, we can develop a standardized method of computationally analyzing each sample
Using this method of textural analysis, we can determine the optical imaging biomarkers most indicative of disease for aid in clinical diagnoses
Contrast
Inverse Difference Moment (Homogeneity)

## Slide 7: Generating the Simulated Dataset
Textural features are the parameters on which the mathematical expressions differentiate between normal and cancerous tissue
Simulated data allows us to understand what visual properties are discerned by textural analysis
A simulated data set was generated to mimic the real tissue samples from a series of five visual parameters
What does the math think cancer looks like?

## Slide 8: Simulated Parameters
  How do the textural features change as a function of simulated image parameters?
3. Circle brightness
4. Overall noise
5. Overall blur
2. Circle thickness
1. Circle radius

## Slide 9: Simulated Results
A subset of simulated images was generated where the circle radius and circle density were increased incrementally
Circle density is a dominant visual feature that affected all of the feature values
  This trend was observed for all five of the introduced parameters (radius, thickness, brightness, noise, and blur)
  All 14 feature values for the parameters were recalculated without the effect of circle density by generating a new simulated data set for a constant circle density
Contrast
Homogeneity
Circle Density
Radius

## Slide 10: Simulated Data Results:
Contrast
Homogeneity
Value of Homogeneity
Image (Value of Contrast)
Image (Value of Homogeneity)
Value of Contrast
Contrast increased as radius increased
Homogeneity increased as radius decreased
Notes: Case for radii

## Slide 11: Real Data Results:
Normal Samples
MAX
Tumor Samples
MAX
Image (Highest Value of Contrast)
Contrast
Image (Highest Value of Contrast)
Value of Contrast
Value of Contrast
Tumor samples demonstrated (on average) a higher value of contrast
Notes: Real data was taken from FAD channel and the middle stack of the sliced sample

## Slide 12: Real Data Results:
MIN
Normal Samples
Tumor Samples
Image (Highest Value of Contrast)
Image (Highest Value of Contrast)
Homogeneity
Value of Homogeneity
Value of Homogeneity
Normal samples demonstrated (on average) a higher value of homogeneity

## Slide 13: Mapping Real Data to Simulated Data
 | Simulated Data |  | Real Data |  | Match Status
Feature # | 1 Circle | 51 Circles | Normal | Tumor | 
1 | Higher | Lower | Lower | Higher | No
2 | Lower | Higher | Lower | Higher | Yes
3 | Higher | Lower | Higher | Lower | Yes
4 | Lower | Higher | Lower | Higher | Yes
5 | Higher | Lower | Lower | Higher | No
6 | Lower | Higher | Lower | Higher | Yes
7 | Lower | Higher | Lower | Higher | Yes
8 | Lower | Higher | Lower | Higher | Yes
9 | Lower | Higher | Lower | Higher | Yes
10 | Higher | Lower | Lower | Higher | No
11 | Lower | Higher | Lower | Higher | Yes
12 | Lower | Higher | Higher | Lower | No
13 | Lower | Higher | Higher | Lower | No
  Tumorous samples often have a greater number of cells (higher circle density) than normal samples
For most features, we have observed the same trend between the real data set and the simulated data set where circle density has been isolated as a parameter
The features which are not correlated with the simulation of circle density may be determined by parameters such as the size of the cells or their brightness

## Slide 14: Discussion & Conclusions
(Near) future work will allow us to determine the specific ranges of feature values for the normal data set and the pathological data set
  Involves testing the identified range of feature values on additional samples to test the accuracy of our model
We may also be able to identify how the features change with other visual parameters such as “streaks” of brightness or patches of noise in the image to better understand how the features change across the real image data set
Eventually, this work will have real applications to patient health
  These results can be used as a metric for an AI algorithm, which will be able to differentiate between normal and tumorous tissue
  Such an algorithm will be able to optimize clinical diagnoses of gastrointestinal and other cancers using optical imaging techniques such as white light endoscopy
  Identifying quantitative biomarkers indicative of disease can alert doctors to perform further screenings and tests, with the goal of improving diagnostic accuracy

## Slide 15: Thank you!

## Slide 16
How do we computationally understand texture?

## Slide 17
Original Image
Grey Level Quantized Image
0 | 7 | 1 | 1 | 0 | 0
7 | 2 | 7 | 3 | 1 | 0
1 | 7 | 6 | 4 | 2 | 1
1 | 3 | 4 | 12 | 7 | 0
0 | 1 | 2 | 7 | 2 | 1
0 | 0 | 1 | 0 | 1 | 0
Horizontal GLCM
Neighbor Pixel
Reference Pixel
0
1
2
3
4
5
0
1
2
3
4
5
1 | 2 | 1 | 2 | 5 | 4 | 3 | 4
0 | 1 | 0 | 1 | 2 | 2 | 4 | 4
3 | 0 | 1 | 2 | 3 | 3 | 2 | 3
3 | 3 | 4 | 3 | 2 | 2 | 3 | 4
4 | 3 | 3 | 1 | 1 | 2 | 1 | 4
3 | 3 | 3 | 1 | 0 | 1 | 2 | 2
2 | 4 | 3 | 3 | 1 | 2 | 0 | 1
0 | 2 | 1 | 1 | 0 | 0
5 | 1 | 2 | 3 | 0 | 0
0 | 7 | 3 | 2 | 0 | 0
0 | 0 | 2 | 6 | 4 | 0
0 | 1 | 2 | 3 | 1 | 1
0 | 0 | 1 | 0 | 0 | 0
Left Neighbor GLCM
Neighbor Pixel
Reference Pixel
0
1
2
3
4
5
0
1
2
3
4
5
0 | 5 | 0 | 0 | 0 | 0
2 | 1 | 7 | 0 | 1 | 0
1 | 2 | 3 | 2 | 2 | 1
1 | 3 | 2 | 6 | 3 | 0
0 | 0 | 0 | 4 | 1 | 0
0 | 0 | 0 | 0 | 1 | 0
Right Neighbor GLCM
Neighbor Pixel
Reference Pixel
0
1
2
3
4
5
0
1
2
3
4
5
+
=
Assembling the Grey Level Cooccurrence Matrix (GLCM)

## Slide 18
Haralick Features
Entropy
Variance

## Slide 19: Qualitative Discussion of Simulated Results
Features 1 and 2 (contrast) seemed to show inverse trends as circle density, radius, thickness, and brightness each individually increased
Features 2 and 4 seemed to demonstrate a similar trend for an increase in circle density
Features 4 and 7 seemed to show similar trends as circle density, radius, and thickness each individually increased
  Features 4 and 6 demonstrated similar trends for circle density, radius, and thickness
  Features 7 and 9 demonstrated similar trends for circle density, radius, and thickness
Features 8 and 9 (entropy) seemed to show similar trends as circle density and brightness each individually increased
Features 12 and 13 seemed to show similar trends for an increase in circle density
Features 10 and 12 seemed to show similar trends for an increase in brightness
Features 9 and 13 seemed to show similar trends for an increase in brightness
Feature 11 was notable as brightness increased since there seemed to be no effect on the feature value