## Slide 1: Intel/TRIF Electrocoagualtion Project
Space Grant Mentor: Profs. James C. Baygents & James Farrell
Research Intern & Presenter: Jake Davis

## Slide 2: Project Purpose & Motivation
Purpose: Assess electrocoagulation (EC) as a technology for municipal and industrial water purification.
  measure removal of: As, Si, Ca, Mg & dissolved organics
Motivation
EC can be used to remove a broad spectrum of contaminants and reduce TSS
EC can be inexpensive and straightforward to implement
Anions associated with chemical coagulants (e.g. Cl and SO42) are avoided with EC—so, EC is salt-free and pH neutral

## Slide 3: EC Flow Through Cell
Water In
Water Out

## Slide 4
EC Flow Through Cell

## Slide 5: Reaching Steady State: Al electrode
Chart: Al Dose (mM) Vs Time (min)
| 2 | 3 | 5 | 9 | 17 | 33
Calc. dose mM | 3.2916 | 3.1048 | 3.3469 | 3.6317 | 4.1357 | 5.3711
Faraday’s law

## Slide 6: Reaching Steady State: Fe electrode
Chart: Dose Fe (mM) vs. Time (min)
| 1 | 2 | 4 | 8 | 16 | 32
 | 0.6341 | 0.88097 | 1.1427 | 1.4238 | 1.7457 | 1.5342
Faraday’s Law

## Slide 7: Contaminant removal: Fe electrode
Chart: % Species Removed vs. Dose Fe (mM) at pH 7
| 0.104050412503628 | 0.17515857551511096 | 0.38197421334107223 | 0.79962688114091496 | 1.014634550806351 | 1.5903735334355964 | 2.0213092326188797 | 3.2589361966750969
% Si removed | 0.10679 | 0.090176 | 0.10679 | 0.2112 | 0.22706 | 0.38286 | 0.53502 | 0.68783
% Ca removed | 0.019232 | 0.013709 | 0.0079384 | 0.045382 | 0.043363 | 0.051923 | 0.073979 | 0.070853
% Mg removed | 0.046881 | 0.033967 | 0.029172 | 0.038802 | 0.051943 | 0.051195 | 0.081025 | 0.092053
Feed Water: silica (50 ppm), calcium (45 ppm), and magnesium (12 ppm)

## Slide 8: Contaminant removal: Fe electrode
Water Composition: arsenic (135 ppm), calcium (45 ppm), and magnesium (12 ppm)

## Slide 9: Contaminant Removal: Fe electrode
Chart: % Species Removed vs. Dose Fe (mM) at pH 7
| 0.1 | 0.2 | 0.4 | 0.8 | 1 | 1.6 | 2
As | 9.2613 | 18.8875 | 31.1964 | 59.9172 | 73.7055 | 89.7662 | 91.9834
Si | 6.4286 | 9.7619 | 15.7143 | 28.8095 | 64.5238 | 48.3333
Ca | 1.4454 | 4.7491 | 8.2903 | 17.0142 | 22.6719 | 24.9226 | 30.797
Mg | 1.7705 | 4.8306 | 7.7596 | 14.4306 | 16.1967 | 18.9421 | 24.8743
Feed Water: arsenic (135 ppm), silica (50 ppm), calcium (45 ppm), and magnesium (12 ppm)

## Slide 10: Summary
The time required for an EC unit to reach steady state is significant
Fe dissolution is approximated by Faraday’s law
Al dissolution is greater than Faraday’s law predicts
EC simply and effectively reduces the arsenic and silica content of municipal and industrial water
The removal of calcium and magnesium from water via EC is positively affected by the presence of arsenic