## Slide 1: Creating a Thermal Shroud
Jessica Avitia
Aerospace Engineering Undergraduate Student
Embry-Riddle Aeronautical University, Prescott AZ
Mentors:
Dr. Ronald Madler
Jack Crabtree

## Slide 2: Reason
For Thermal System Detail Group
Future payload testing

## Slide 3: Project Goal
Create a thermal shroud to simulate space environment
Create a thermal plate prototype to test the concept
Create a thermal shroud from the prototype

## Slide 4: Heat Transfer
(sciencelearn, 2009)

## Slide 5: Heat Transfer

## Slide 6: Background
Thermal Shrouds simulate space environment
Place inside vacuum chambers
Helps the system reach equilibrium temperatures
(Angstromengineering, 2010)

## Slide 7: Experimentation
Researched Thermal Shrouds
  Material properties / liquid nitrogen
Created a thermal plate prototype for testing
Adjusted thermal plate
Created a thermal shroud for thermal systems detail design group

## Slide 8: Thermal Plate
¼ inch 2024 aluminum plate

## Slide 9: Thermal Plate
Type K copper tubing
½ inch inner diameter

## Slide 10: Testing
10 thermocouples placed on thermal plate
Drop vacuum chamber to 0.038 Torr (pressure)
Ran liquid nitrogen for one hour
Recorded data from thermocouples
4
2
1
3
5
8
7
6
9
10

## Slide 11: After Experiment

## Slide 12
Chart: Test # 1
1 | 69 | 69 | 69 | 69 | 69 | 69 | 69 | 69 | 69 | 69
2 | 71 | 70 | 71 | 69 | 70 | 70 | 69 | 69 | 68 | 69
3 | 72 | 62 | 74 | 63 | 71 | 59 | 57 | 59 | 57 | -6
4 | 56 | 64 | 62 | 72 | 71 | 61 | 58 | 62 | 58 | 37
5 | 62 | 64 | 71 | 62 | 71 | 61 | 59 | 64 | 59 | 52
6 | 46 | 57 | 71 | 55 | 71 | 42 | 13 | 45 | 42 | -2
7 | 12 | 41 | 71 | 36 | 71 | 17 | -14 | 26 | 14 | -12
8 | 10 | 29 | 71 | 22 | 71 | -2 | -36 | 1 | -8 | -122
9 | 32 | -7 | 71 | -8 | 71 | -40 | -67 | -43 | -45 | -175
10 | 65 | -19 | 72 | -18 | 71 | -31 | -37 | -27 | -39 | -177

## Slide 13: Results
Thermocouples and liquid nitrogen behaved as expected
Thermal plate reached a temperature of approximately -250 °F

## Slide 14: Conclusion
From my thermal plate prototype Thermal System Detail Group was able to create a full size thermal shroud
(GES,2009)

## Slide 15
(GES,2009)
(GES,2009)

## Slide 16: Acknowledgements
Dr. Madler
Jack Crabtree
Chris Smith
Dr. Haven
Thermal System Detail Group
NASA Space Grant
Questions????