## Slide 1: CFD Study of the Development of Vortices on a Ring Wing
Kyle Wright
Embry-Riddle Aeronautical University
Prescott, Arizona

## Slide 2: Overview
Background
  Wingtip Vortices
  Wingtip Devices
  Ring Wings
  Computational Fluid Dynamics (CFD)
Introduction
Geometry
Mesh
Solver & Boundary Conditions
Results
Conclusion

## Slide 3: Background: Wing-Tip Vortices

## Slide 4: Background: Wingtip Devices
Wingtip Devices: aim to reduce wingtip vortices by decreasing vorticity magnitude and/or moving location away from wing surface to reduce induced drag
Boeing 737 Winglet
(Source: westjet.com)

## Slide 5: Background: Ring Wings
Ring Wing
  Wingtips wrap around to enclose entire wing
  Type of closed wing (cylindrical, joined, box wings)
  Has no actual wingtips
  Decreases induced drag to increase efficiency
Selex Galileo – Asio Ring Wing UAV
(Source: flightglobal.com)

## Slide 6: Background: CFD
Aerodynamic Analysis
Experiential Analysis
Computational Fluid Dynamics Analysis
Analytical Analysis
Computational Fluid Dynamics
  Numerical method of solving partial differential equations for viscous fluid flow (Navier-Stokes Equations)
  Mesh or discretize flow domain into a structured or unstructured grid to create small finite volumes
  Numerically iterate through flow domain matrix with boundary conditions until solution has converged

## Slide 7: Introduction
Ring Wing in 2x2ft blower wind tunnel
(Source: Traub, Lance, “Experimental Investigation of Annular Wing Aerodynamics”,
Journal of Aircraft, Vol. 46, No. 3, 2009, pp. 988-996)
Tuft-grid in wake of ring wing
(Source: Fletcher, Herman, “Experimental Investigation of Lift, Drag, and Pitching Moment of Five Annular Airfoils”, NACA TN4117, 1957 )
Experimental work done by Dr. Lance Traub and students inspired this CFD study, Re = 225,000, V∞ = 40 m/s, Chord = 0.1m≈4 in
Goals
  Compare/Match CFD results to experimental work
  Show the development of wingtip vortices

## Slide 8: Geometry (CATIA)
Diameter – 8 in
Chord Length – 4 in
Aspect Ratio – 2

## Slide 9: Mesh (GAMBIT)
Average # tetrahedral volumes ≈ 362000

## Slide 10: Solver (Fluent) & Boundary Conditions
Symmetry
Velocity inlet
Outflow outlet
Wall – Top,
Bottom, and
Right faces
12 in
12 in
24 in
24 in
Pressure based solution from low experimental Reynolds number
Viscous Model: Spalart-Allmaras (single equation)
Density & Viscosity: 1.05 kg/m3 & 1.896e-5 kg/(m s) to match experimental Reynolds number
Inlet: Velocity Inlet at 40 m/s with 0.5% turbulence intensity ratio

## Slide 11: Results: Lift and Drag Coefficient Plots
Chart: Lift Coefficient
| 1.2 | 1.21 | 1.21 | 1.28 | 1.1700000000000021 | 1 | 0.33000000000000101 | -0.14000000000000001
Experimental [Traub] | 0.725 | 0.66 | 0.52 | 0.4 | 0.28 | 0.22 | 0.1 | 0.1
Numerical (CFD) | 0.73071 | 0.66166 | 0.38604 | 0.33332 | 0.24222 | 0.16886 | 0.071368 | 0.077648
Chart: AOA
| 28 | 26 | 24 | 22 | 20 | 18 | 16 | 14 | 12 | 10 | 8 | 6 | 4 | 2 | 0 | -2 | -4 | -6
Experimental [Traub] | 1.2 | 1.21 | 1.21 | 1.28 | 1.17 | 1 | 0.33 | -0.14
Numerical (CFD) | 1.4994 | 1.5651 | 1.6783 | 1.6174 | 1.385 | 1.0933 | 0.26476 | -0.24677

## Slide 12: Results: Velocity Pathlines

## Slide 13: Results: Pressure Contour Plots, AoA = 14°
Sweep surface plots for AoA = 14° (Pa)
x = 0 in
x = 2 in
x = 3 in
x = 4 in
x = 5 in
x = 6 in
x = 7 in
x = 8 in

## Slide 14: Results: Pressure Contour Plots, AoA = 20°
Sweep surface plots for AoA = 20° (Pa)
x = 0 in
x = 2 in
x = 3 in
x = 4 in
x = 5 in
x = 6 in
x = 7 in
x = 8 in

## Slide 15: Conclusion
CFD results followed lift and drag trends of experimental work, especially at lower AoA
CFD results showed the development of two main vortices in the wake region of ring wing

## Slide 16: Questions