## Slide 1
Kenneth Geshell, David J. You, Jeong-Yeol Yoon
Biosensors Laboratory
Agricultural & Biosystems Engineering
University of Arizona
Detection of Escherichia coli in lettuce samples
Food and Water Quality Monitoring

## Slide 2: Introduction
Escherichia coli is a leading cause of food-borne disease.
Outbreaks of Escherichia coli O157:H7 is prevalent
  2006: E. coli found in Dole bagged fresh spinach; 200 illnesses and 3 deaths.
  2006: E. coli found in Taco Bell lettuce; 53 hospitalized.
  2008: E. coli outbreak in Michigan in iceberg lettuce from California; 36 illnesses

## Slide 3: Current Methods
Conventional culturing and colony counting
  Requires days for culturing and skilled personel.
Enzyme-linked immunosorbent assay (ELISA)
  Requires multiple steps of reagent addition and rinsing. Too complex to use in the field.
Polymerase chain reaction (PCR)
  Requires pre-designed primers.

## Slide 4: Background
Sensing Element: Immunoaffinity
  Sample fluid is mixed with particle solution, and target cells are captured by antibody-antigen binding
  This causes particles to adhere together in clumps

## Slide 5: Background
Transducing Element: Light Scattering
A light beam focused through the solution is scattered according to particle size.
Light scattering is directly related to quantity of target in the sample solution.

## Slide 6: Chip-on-a-lab

## Slide 7: Background Summary
Transduction method of light scattering of immunoagglutinated particles provides a rapid and portable solution to pathogen detection required for agriculture
Chip-on-a-lab methodology shows high sensitivity of less than 10 cfu/mL
Preliminary results for differential two-well slide device show high reproducibility and sensitivity to 103 cfu/mL
  Distinguishable signal at 102 cfu/mL
  Unsteady voltage output due to particles entering and leaving focal region

## Slide 8: Using Lettuce Samples
I expanded the previous work to include testing on samples of actual lettuce.
This was done by grinding up iceberg lettuce samples with a mortar and pestle then adding this lettuce to PBS. 2mL PBS for each gram of lettuce (wet weight).

## Slide 12
Chart: 
| 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1
0sec | 1.5064 | 1.1434 | 1.0464 | 1.0086 | 1.0487 | 1.0295 | 1.0961 | 1.0247 | 1
30sec | 1.5013 | 1.1565 | 1.0539 | 0.99563 | 1.0417 | 1.025 | 1.1015 | 1.0221 | 1
60sec | 1.5024 | 1.1668 | 1.075 | 1.0285 | 1.0458 | 1.0295 | 1.105 | 1.0329 | 1
Blank 10-7 10-6 10-5 10-4 10-3 10-7 10-1 1
Concentration of E.Coli
Normalized Intensity Readings
Effect of Time on the Agglutination of the Particles/ Reading

## Slide 13
Chart: 
| 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1
Chip-On-A-Lab | 1.4565 | 1.1486 | 1.0744 | 1.0458 | 1.0568 | 1.0329 | 1.0953 | 1.0536 | 1
Blank 100 1000 104 105 106 107 108 109
CFU
I
__
I0

## Slide 14
Chart: 
| 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1
 | 1.5497 | 1.1482 | 1.1603 | 1.1346 | 1.1528 | 1.1507 | 1.1298 | 1.0935 | 1.0804 | 1.0078 | 1
 | 1.1507 | 1.1298 | 1.0935 | 1.0804 | 1.0078 | 1
Blank 100 1000 104 105 106 107 108 109 1010
CFU
Normalized Intensity Readings
Chip-on-a-lab Data for 50% standard concentration with 920nm beads

## Slide 15: Future Work
Reconstructing the Prototype device
Test other vegetables
microfluidic device.
Optimize particle size and concentration

## Slide 16: Acknowledgements
Special thanks to:
  David You
  Jeong-Yeol Yoon
  Brian Heinze
  Phat Tran
  Jin-hee Han (UC Davism)
  Lonnie Lucas (Arete, Inc.)
  Austin Folley (Ohio State Med)
  Emma Setterington (U of Michigan)
This work was supported by:
  NVQRS
  Desert Tech