## Slide 1: Transient Radiation Effects Behavioral Modeling
David Oleksy, Electrical Engineering
Hugh Barnaby, Bert Vermeire, Craig Birtcher, ASU, Stephen Buchner, NRL
2009 – 2010 Statewide Symposium
Arizona Space Grant Consortium
Kuiper Space Sciences / LPL, April 17, 2010

## Slide 2: Problem Statement
Increasing sophistication of space and strategic systems
Radiation hardness demands of some missions
New predictive modeling capabilities must be developed to support system design prior to test and integration

## Slide 3: Radiation Effects of Concern
We are focused on errors caused by high energy ion exposures, which lead to single event effects and transients
In example:
A memory module’s stored data can be corrupted when struck by a high energy particle
In this study:
The output of a voltage regulator deviates from the nominal voltage when certain nodes are irradiated

## Slide 4: Project Tasks
Our first effort focuses on the delivery of a radiation-enabled macro-model for a Raytheon system component
Targeted component: LT1129 3.3V Voltage Regulator
Project deliverables:
Deliverable | Related Task | Description | Status
LT1129 standard macro-model | Task 1 | Build standard macro model of LT1129 voltage regulator circuit | complete
LT1129 laser data report | Task 2 | Report the results of laser testing for transient characterization in IC | complete
LT1129 full transient-enabled macro-model | Task 3 | Full report and SET model of LT1129 IC with calibrated SET signal set | In progress

## Slide 5: Task 1 – Standard Macro-model
with additions
* OUT ADJ GND SHD IN
.SUBCKT LT1129 1 2 3 4 5
QPWR 51 54 52 Q1
RBASE 54 53 16100
DDARl 53 84 DX
RDROP 51 1 0.4 TC=4.0E-3
RQC 1 3 106E3
VCURR 5 52 DC 0
FGND 5 3 POLY(1) VCURR 8.5E-6 0 0.097
FCL1 3 60 VCURR 0.31
RCL1 60 3 10
DCL1 60 61 DX
VCL1 61 62 DC 0
ECL1 62 3 POLY(1) 5 3 2.75 0.035
FCL2 90 3 VCL1 1.0
IBSD 5 4 DC 6.0E-6
DSDP1 4 70 DX
VSDP1 70 3 DC 6.2
DSDN1 71 4 DX
VSDN1 71 3 DC 0.595
GSD1 3 73 72 4 1.0E-1
RSD1 73 3 1.0E4
CSD1 73 3 2.2E-9
GTV1 3 72 POLY(1) 73 3 0.78E-3 1.20E-4
RTV1 72 3 1.0E3
DSDP2 73 74 DX
VSDP2 74 3 DC 2.90
DSDN2 75 73 DX
VSDN2 75 3 DC 0.85
QSD 90 77 3 Q2
RSD3 77 3 1.0E1
GSD3 3 77 73 3 5.3E-2
IBEA 3 80 DC 148.7E-6
REA1 80 3 1.0E3 TC=-4.6E-3
GEA1 2 3 80 3 1.0E-6
DEAP1 2 81 DX
VEAP1 81 3 DC 5.3
DEAN1 82 2 DX
VEAN1 82 3 DC 0.4
GEA2 3 84 2 90 10.0
REA2 84 3 1.0E3
CFEED 84 88 1e-8
RFEED 88 90 2.0E3
DREV 5 55 DX
RREV 55 3 1.0E9
DEAP2 84 85 DX
EEAP2 85 3 POLY(1) 55 3 -1.0 1.0
DEAN2 86 84 DX
VEAN2 86 3 DC 1.0
IREF1 3 90 DC 3.7502E-3
RREF1 90 3 1.0E3 TC=1.0E-4
GLINE 3 90 5 3 1.3E-8
GLOAD 90 3 51 1 24.6E-6
.MODEL DX D IS=8e-16 RS=0 XTI=0
.MODEL Q1 PNP IS=1e-12 BF=11400 XTI=0
.MODEL Q2 NPN IS=1e-16 BF=1000 XTI=0
.ENDS LT1129
Schematics by David Oleksy with help from Bert Vermeire

## Slide 6: Task 2 – Laser Testing Prep
Photo by
David Oleksy
Photo by David Wright and David Oleksy

## Slide 7: Task 2 – Laser Testing Prep
All graphics by David Oleksy
• Package chip
• Design test board
• Order the board
• Populate board
• Write manual

## Slide 8: Task 2 – Laser Testing
Results by Stephen Buchner
Example of data set:
Highlighted strike locations that produce similar measurable voltage output effects

## Slide 9: Task 3 – TRE Enabled Model
Model development is in progress
Radiation strikes are simulated with directly applied spikes of current on certain circuit nodes
Simulated strikes on some nodes already match the data…
Hugh Barnaby
Hugh Barnaby
Stephen Buchner
Double Exp. Current Spike

## Slide 10: Current Conclusions
Laser testing is an effective means of measuring transients in linear microcircuits
It is advised to consider development of a laser system as a stand-alone characterization and modeling tool
It is advised to establish collaboration between Raytheon and ASU to progress appropriately and integrate with Raytheon’s TopACT code
Laser test data used with macro-model is cheaper, quicker and more powerful.
TRE enabled macro-models allow better system design

## Slide 11: That’s it!
Thank you for listening
Please ask any questions you may have