## Slide 1: Nanowires and Heterostructures
Michael Christiansen
Mentor: Dr. Jeff Drucker
Statewide Space Grant Symposium
17 April 2010
Special thanks to: Jeff Drucker, Nick Jungwirth, Sutharsan Ketharanathan, Prashanth Madras, and Eric Dailey

## Slide 2: Nanowires
Made of the Group IV elements silicon and germanium
Length is generally about 1𝜇m and diameter is 10 to 100 nm
500nm
“One dimensional” nanostructures, approximately cylindrical
May contribute to applications such as photovoltaics, thermoelectrics, and nanoelectronics
(SEM, courtesy of Jeff Drucker)

## Slide 3: Vapor-Liquid-Solid Growth Process
Thermal deposition of metal catalyst (e.g. gold), forming droplets that are a liquid mixture of silicon and gold
Addition of silicon or germanium to the droplet (via reaction of Si2H6 or Ge2H6) results in crystal growth outward from the substrate
(Diagram courtesy of Jeff Drucker)
(Graph from Scientific Thermodata Group Europe, www.sgte.org)

## Slide 4: Axial Heterostructures: Our Project
Grown by switching between adding silicon and adding germanium, resulting in alternating segments
Two main challenges:
An atomically abrupt transition between silicon and germanium is desirable.
Sidewall deposition needs to be minimized.
Our project: to investigate thermal deposition of alternative metal catalysts
(TEM, courtesy of Jeff Drucker)

## Slide 5: Gold vs. Indium
(Graphs from Scientific Thermodata Group Europe, www.sgte.org)

## Slide 6: Progress
Construction of ultrahigh vacuum chamber (target pressure 10-9 Torr, or 1/1012 atm)
Transfer mechanism for samples
Calibration of In evaporation source
Characterization of substrate heating

## Slide 7: Thanks for listening. Questions?
(TEMs, courtesy of Prashanth Madras)