## Slide 1: Optimizing Attitude Determination for Sun Devil Satellite – 1
Michelle Smith
Attitude Control Subsystem

## Slide 2: Topic Overview
Attitude Control System
Quaternion Parameterization
Kalman Filter Application
Results of Implementation

## Slide 3: Attitude Control System
Essentially comprised of…
  Sensors—
        magnetometer
        fine sun sensor
        course sun sensors (photodiodes)
        inertial measuring unit
  Actuators—
        reaction wheels
        magnetorquers
  Associated Errors and Inaccuracies
Simplified Attitude Control System Model

## Slide 4: Parameterization
Quaternion:
  A four dimensional vector used to describe three dimensions, defined as
  with
  ***quaternion components cannot be linearly independent
  Satisfy normalization constraint :
Advantages
  The attitude matrix is quadratic in parameters, so no transcendental functions
  For small angles, vector part and
  Kinematics equation is linear and free of singularities
  Rotations easily accomplished using quaternion multiplication

## Slide 5: Kalman Filter Application
Kalman Filter: recursive algorithm which produces an optimal estimation of a system state from noisy input data
Can be thought of as…
    Collection of Subroutines
              Initialize
              Gain
              Update
              Propagation

## Slide 6: Kalman Filter Application
ROUTINE
The filter is initialized with a known state and error covariance matrix [attitude errors]
Kalman gain computed using measurement error covariance and sensitivity matrix
Updates and the quaternion renormalized
Estimates angular velocity used to propagate quaternion kinematics model and standard error covariance in the Kalman Filter

## Slide 7: Kalman Filter Application
Beginning with quaternion kinematics model, given by
Use(“Add”) equation directly in Kalman Filter
      Problem: destroys normalization constraint
      Solution: using multiplicative error quaternion in body frame
      First order approximation assumes true quaternion is close to estimated  reduces system by one state

## Slide 8: Kalman Filter Application
Next sensitivity matrix must be determined from discrete time attitude observations
      vector measurements from n sensors concatenated
  Each (estimation) sensor vector is given by:
Substituting into the approximation of error attitude matrix
where is small angle approx.
Yields...
sensitivity matrix for all measurement sets

## Slide 9: Kalman Filter Application
Finally  the error-state and quaternion update
Error State Update:
measurement output
estimate output
Kalman gain
          Quaternion Update:
          +
          ***renormalization should be performed to insure unity
Showing Recursive Property of Kalman Filter

## Slide 10: Expected Results of Implementation
Implementation still in progress…
Qualitative Results
  By introducing the Kalman Filter into Sun Devil Satellite-1’s control system, attitude determination is expected to be optimized
    Increased accuracy with minimal additional computational burden
Quantitative Results
  How will it be tested?
  Simulation
    Reference attitude matrix (true attitude)
    Introduce Gaussian noise
    Compare outputs from attitude simulation
      without Kalman Filter
      with Kalman Filter
      actual/reference attitude
  Ensure quaternion normalization
Quaternion Normalization Results

## Slide 11: Questions or Comments?
Name: Michelle Smith
Website: http://sdsl.club.asu.edu/
Email: sdsl@asu.edu
or msmith28@asu.edu