## Slide 1: Micro Subglacial Lake Exploration Device (MSLED)
Student: Daming Chen
Mentor: Dr. Alberto Behar
http://extremerobotics.lab.asu.edu

## Slide 2: Antarctic Subglacial Lakes
Located deep beneath ice sheet in bedrock
Part of an interconnected system of water drainage
Influences ice sheet movement and melt
May harbor unique ecosystems
Analog for extraterrestrial bodies
Whillans
Ice Stream

## Slide 3: WISSARD Project
Whillans Ice Stream Subglacial Access Research Drilling
  GeomicroBiology of Antarctic Subglacial Environments (GBASE)
  Lake and Ice Stream Subglacial Access Research Drilling (LISSARD)
  Robotics Access to Grounding-zones for Exploration and Science (RAGES)
Notes: Ross Ice SHelf

## Slide 4: MSLED Objectives
Investigate water-ice interface
Determine structure of water column
  Physical: Pressure and temperature
  Chemical: Salinity and pH
  Visual inspection
Visually investigate lake floor for geologic and sedimentary processes
Look for biological features

## Slide 5: System Requirements
Operate for minimum 2 hr
Two-way communication with surface in real-time
Return to the borehole for retrieval
Operate in temperatures from -10°C to 50°C
Utilization of commercial-off-the-shelf components
Withstand decontamination for clean access
Utilization of existing infrastructure (Ice Borehole Probe)
Sensors: high resolution video, temperature, salinity and pressure
Operational range of 1 km
Operating at depth up to 1.5 km
Maximum 8 cm diameter and 70 cm length
Remotely operated from surface
Localization of measurements
Notes: Form factor constraints (borehole, mission)
High pressures (environment)
Low temperature (environment)
High bandwidth communication with surface (payload)

## Slide 6: System Design
Background image: Flickr, WoaH

## Slide 7: Structure
Background image: Flickr, WoaH
Electronics Compartment
Nose Cone with Window
Flooded Chamber for Fiber Spool
Liquid Compensated Servo Motors
Propeller with Kort Nozzle
Main Motor Cavity

## Slide 8: Internal Components
Camera
(Prosilica GC1380C)
Fiber Transceiver
(Prizm TEL Series Gigabit )
CTD Sensor
(Star Oddi CTD DST)
Fin Servos
Background image: Flickr, WoaH
Fiber Spool (Linden Photonics)
IMU
(MicroStrain 3DM-GX3-25)
Battery Pack
(SAFT LSH 14)
Brushless Motor
(Exceed RC Optima)
Buoyancy
Engine
Command and Data Handling
(ATmega2560)
LED light ring
(Cree XLamp XP-E)

## Slide 9: Software Design
Controlled through the fiber optic connection from MSLED
Software written in C# and makes use of the XNA framework to communicate with XBOX360 controller
Draws bitmaps to screen from camera API, with OSD overlay on top for temperature, humidity, thrust, voltage, current, heading, and pitch

## Slide 10: Antarctic Testing

## Slide 11: Chase Vehicle

## Slide 12: Current Status
2011 – Field Test Deployment
  McMurdo Station (November-December)
2012 – Possible re-test
  McMurdo Station with full system
2013/2014 – Field Deployment
  WISSARD:
    Whillans Ice Stream Antarctica
Ongoing Testing
  Lake Tahoe
  Crater Lake
  Arizona Lakes
  Pools

## Slide 13: Questions & Comments