## Slide 1: Project ASCEND!
Embry-Riddle Aeronautical University
Spring 2014
Presented By:
Ankit Jain – Project Manager

## Slide 2: Team Organization
Ankit Jain: Project Manager
Ben Anderson: Assistant Project Manager
Patrick Deskin: System Integrator
Brigette Cochran: Software Engineer
Dallas Hodge: Hardware Engineer
Austin Leonard: Structural Engineer
Loren Williams: Structural Engineer

## Slide 3: Presentation Overview
Project Overview
Computer Aided Design (CAD) & Rapid Prototyping
Fabrication
Hardware & Software
Attitude Determination
Flight Results
Future Developments
Acknowledgments

## Slide 4: Project Overview
Accurate attitude determination
Real-time implementation
PCB manufacturing
26-sided structure
Booms for stabilization
Standard clamp rod attachment

## Slide 5: CAD & Rapid Prototyping

## Slide 6: Early CAD Design
CATIA V5 R17

## Slide 7: Final CAD Design
Red: Switch Mount
Blue: IMU and Power Regulator Mount
Yellow: 9V Battery Mount
Purple: PCB and Data Logger Mount
Green: Camera Mount

## Slide 8: Rapid Prototyping

## Slide 9: Fabrication

## Slide 10: Fabrication
Bi-directional carbon
NOMEX honeycomb
2/10” styrofoam insulation

## Slide 11: Fabrication
Epoxy
Fiberglass reinforcement
Microballoons

## Slide 12: Fabrication
Lexan plate for camera window
Velcro door mechanism

## Slide 13: Assembly
All mounts are removable
Bolted into place
Central rod holds all mounts in place
Booms screw into
mounting block

## Slide 14: Hardware & Software

## Slide 15: Flight Software / Hardware
Dr. Isenberg’s data logging system utilizing a PIC processor
3.3V and 5V power regulators
IMU board
PCB – signal routing & conditioning
Video recorder
Data Analysis: MATLAB

## Slide 16: Attitude Determination

## Slide 17: Attitude Determination
23 solar panels as sun sensors
IMU consisting of a 3-axis rate gyroscope and 3-axis accelerometer
Two vector attitude determination using Wahba’s Problem
  Acceleration Vector
  Sunlight Vector

## Slide 18: IMU Calibration
Both rate gyroscope and accelerometer calibrated
Cross-coupling effects considered between axes
Verification of calibration

## Slide 19: Light Measurement Vector
Orientation of each panel with respect to x, y, and z axes of gondola (i.e., body frame)
Transformation of data into light measurement vector with respect to the body frame

## Slide 20: Flight Results

## Slide 21: Acceleration Vector

## Slide 22: Angular Velocity Vector

## Slide 23: Light Measurement Vector

## Slide 24: Attitude (Quaternion)

## Slide 25: Results Comparison

## Slide 26: Future Developments
Recruit more software engineers
Debug I2C
Complete external SD & file system
Real-time implementation
Moving to C++ for libraries containing array math
Determine better attitude estimation algorithm
Attitude control

## Slide 27: Acknowledgements
Jack Crabtree – ERAU & ANSR
Dr. Gary Yale - ERAU
Dr. Douglas Isenberg - ERAU
Jim Weber – ERAU
Dr. Brian Davis - ERAU
Patrick David - ERAU
Chris Smith – ERAU
Ben Ellefson – Powerfilm Solar
NASA Space Grant Members
University of Arizona