## Slide 1: Bioremediation of Arsenic Contaminated Water
23rd Annual Arizona Space Grant Consortium Symposium
The University of Arizona, Tucson, AZ
April 12th, 2014
Sarah Moore
Lucia Rodriguez-Freire, Dr. James Field, and Dr. Reyes Sierra
Department of Chemical and Environmental Engineering
The University of Arizona

## Slide 2: Outline
Arsenic Background and Theory
Project Objectives
Experimental Methods
Results
Conclusions
Continued Work

## Slide 3: Arsenic Background
Arsenic (As) is an important water contaminant
  Toxicity
  Carcinogenicity
  Widespread occurrence
  Natural and Industrial
Source: http://www.water-research.net/arsenic.htm

## Slide 4: The Arsenic Cycle
Arsenic occurs in several forms: Dissolved cations (AsIII and AsV), elemental As, organic As, arsenic sulfide minerals
Microorganisms play an important role in the arsenic cycle
AsV

AsIII

Trimethylarsine
Water

## Slide 5: Arsenic Sulfide Biomineralization
Source: Lucia Rodriguez-Freire

## Slide 6: Objectives
Investigate the possibility of bioremediation of arsenic contaminated water
Process of anaerobic biomineralization
Explore implementation of continuous biological reactors

## Slide 7: Methods
AsV, SO42-, food
AsV, food,
NO SO42-
AsV AsIII
SO42- S2-
AsIII+ S2-

As2S3 (Solid)
AsV AsIII
Complete Treatment: Biomineralization
Control:
No Biomineralization
S2-, AsIII (reduced amount), byproducts
AsIII, byproducts

## Slide 8: Results
Day 0
Day 154

## Slide 9: Electron Microscope Image
Source: University Spectroscopy and Imaging Facility (USIF)

## Slide 10: Arsenic Concentration: Complete Treatment
Chart: Time (days)
| 84.0 | 85.0 | 86.0 | 87.0 | 89.0 | 91.0 | 93.0 | 96.0 | 99.0 | 101.0 | 104.0 | 106.0 | 107.0 | 109.0 | 112.0 | 115.0 | 118.0 | 121.0 | 123.0 | 126.0 | 128.0 | 131.0 | 134.0 | 137.0 | 140.0 | 143.0 | 145.0 | 148.0 | 150.0 | 152.0 | 154.0 | 156.0
Influent

## Slide 11: Arsenic Concentration: Control
Chart: Time (days)

## Slide 12: Percent Arsenic Removal
Chart: Time (days)

## Slide 13: Conclusions
Arsenic-sulfide minerals can be formed in anaerobic continuous bioreactors
An average of 92% of the total As was removed in the complete treatment
Arsenic biomineralization can be used to remediate arsenic contaminated water

## Slide 14: Continued Work
Long term mineral stability experiments
  At pH = 6.5, less than 1% of mineral dissolved
  At pH = 7.5, significant amount of mineral dissolved
Design of bioremediation system that implements biomineralization
  In situ
  Pump and treat
  Permeable Reactive Barrier

## Slide 15: Thank You!
Special thanks to my mentors, Lucia Rodriguez-Freire, Dr. James Field, and Dr. Reyes Sierra, the UA Chemical and Environmental Engineering Department, University Spectroscopy and Imaging Facility (USIF), Robert Root (UA) and Stanford Synchrotron Radiation Laboratory (SSRL), NASA and the Arizona Space Grant Consortium.

## Slide 16: Extra Slides for Questions

## Slide 17: Reactor Specifics
Complete Treatment Influent
  1 mM AsV
  1.5 mM SO42-
  4.5 mM Ethanol
  Minerals
Control Influent
  1 mM AsV
  4.5 mM Ethanol
  Minerals
Analytical Techniques
  Ethanol and Acetate: Gas Chromatography
  SO42- and AsV: Ion Chromatography
  Sulfide: Colorimetric Methods
  Total As: Inductively Coupled Plasma

## Slide 18: In Situ Bioremediation
Source: Lucia Rodriguez-Freire

## Slide 19: Permeable Reactive Barrier Bioremediation
Source: http://eg.geoscienceworld.org/content/8/4/258/F1.expansion.html