## Slide 1: Nano-Copper Inhibition of Anaerobic Digestion in Wastewater Treatment
Sara J Gallagher, Jorge Gonzalez-Estrella,
Jim Field, and Reyes Sierra-Alvarez
22nd Annual AZ Space Grant Consortium Symposium
April 12th, 2014

## Slide 2: What Are Nano-Particles?
Nano-particles (NPs)
Discharged in sewage pipelines to wastewater treatment plants
Cu0 NPs INHIBIT methane-producing microorganisms (methanogens).
Image source: http://www.hermione-presents.com/back_home/back_home%20tours.htm

## Slide 3
Why Are Nano-Particles Important?
Nano-particles (NPs) are currently used in large quantities in many common consumer products, including toiletries and personal-care items.
Research has indicated that some types of NPs have toxic effects on human health and the environment.
Image source: http://www.westcoastcosmetics.com/

## Slide 4: The Biochemistry
Start Here
OR Start Here
End
Image source: www.wtert.eu

## Slide 5: Objectives
To determine how the addition of Cu0 NPs affects:
The consumption of glucose/propionate and
The production of methane (CH4) by
microorganisms involved in anaerobic digestion.

## Slide 6: Procedure
Different concentrations
Overnight incubation
GC-TCD
Anaerobic granular sludge
N2/CO2
Dispersion of NPs
Electron donor: glucose or propionate
T (35°C), 115 rpm
Propionate and CH4
Glucose

## Slide 7
20 ppm Cu0 NP decreased the maximum consumption glucose rate
by 3x.
IC50 = 7 ppm

## Slide 8
20 and 40 ppm Cu0 NP decreased the maximum propionate consumption rate by 3x and 4x respectively.
IC50 = 15 ppm

## Slide 9
Inhibition of Methanogenesis in Assays Supplied with Glucose and Propionate
Methanogenesis was more inhibited by nano-Cu in assays
using propionate as a substrate.
IC50 = 10 mg L-1 Cu0 NPs
(substrate: propionate)
IC50 = 20 mg L-1 Cu0 NPs
(substrate: glucose)

## Slide 10: Conclusions
    Cu0 NP are toxic to various anaerobic microbial populations including methanogens as well as glucose- and propionate-degrading microorganisms.
    Low concentrations of nano-Cu (≥ 5 ppm) can cause serious inhibition of anaerobic digestion processes.

## Slide 11: Acknowledgments
Mentoring and lab access: Dr. Reyes Sierra and
Dr. Jim Field
PhD candidate: Jorge Gonzalez-Estrella
Facilities: The University of Arizona
Program: Arizona NASA Space Grant Consortium