## Slide 1: Pima community college-west atmospheric particle collection Project: Electronics
Electronics Team
Roslyn Norman
Noelia Parraz
Jonathan Parker
Kyle Gordon
ASCEND! FLIGHT 22 / ANSR FLIGHT 97
Notes: Speaker: Dr. Silvia Kolchens

## Slide 2: Electrical goals
FALL SEMESTER
Rotate particle collection wheel at specific intervals using:
  Arduino Nano
  BMP180 altimeter sensor
  Hall effect sensor
  Altered servo motor
SPRING SEMESTER
Rotate particle collection wheel at specific intervals using:
  Arduino Uno
  BMP180 altimeter sensor
  Stepper Motor / Driver
Collect ozone data
Collect comparative altimeter date using Parallax sensor
Notes: Speaker: Kyle Gordon
Talk about the differences between the semesters. ( Arduino Nano v Arduino Uno )
How the Servo was Altered.
(Stepper v Servo)

## Slide 3
FALL SEMESTER
SPRING SEMESTER

## Slide 4: Fall semester data
Chart: Altitude vs Time
Balloon Burst
Power Loss
Notes: Speaker: Roslyn Norman
Launch Time –30mins after powered on
Max – 74,000FT (same as actual within a few hundred feet) –1.5hrs into flight
Power Loss – 26,000FT (parachute deployment) --2hrs into flight

## Slide 5: Fall semester data
Chart: Time (y-axis) vs Temp (x-axis)
Launch Time
Balloon Burst
Notes: Temp Sensor was inside the payload
Temp Max: 66F / 19C (above inversion layer) – 16,000FT –42mins into flight
Temp at time of burst: -15F / -26C
Temp Min -31F / -35C –26,000FT –2Hrs ( colder b/c more air flowing through payload )  About the temp in Chicago in winter

## Slide 6: Fall semester data
Chart: Pressure (hPa) vs Time
Launch Time
Balloon Burst
Notes: Close to vacuum conditions at apex

## Slide 7
Balloon Burst

## Slide 8: Spring semester data
DATA COLLECTION COMPROMISED BY ELECTRICAL FAILURE
WHY THE CIRCUIT FAILED:
Circuit was overloaded.
Too many components drawing power from a single Uno board caused the processor to overheat and shut down.
Notes: Speaker: Jonathan Parker

## Slide 9: conclusions
FALL SEMESTER
Experiment considered successful.
Data collected- accurately depicted ascent / descent.
Particle samples from each atmospheric interval were collected and analyzed successfully.
SPRING SEMESTER
Using stepper motor is more accurate than servo motor / hall effect set up, but draws more power.
Need more than one micro processor to run all components.
Notes: Speaker: Noelia Parraz

## Slide 10: ACKNOWLEDGMENTS
Tim Swindle (Space Grant Director)
Susan Brew (Space Grant Manager)
Jack Crabtree (ANSR)
Silvia Kolchens (PCC Mentor)
ANSR Volunteers
Xerocraft, Hacker Space

## Slide 11: Questions?