## Slide 1: Mesh Refinement: Aiding Research in Synthetic Jet Actuation
By:
Brian Cowley

## Slide 2: Background – Definition and Implementation:
Synthetic Jet flow actuation is a method for controlling airflow over airplane wings
Implementation:
  Electrodes over leading edge
  High frequency pulse from boot-like actuators
Standard Boot Actuator:
Internal Structure:

## Slide 3: Background – Benefits and Results:
Benefits:
  Reduced boundary layer thickness (Translates to reduction in drag)
  Delays the onset of boundary layer separation at high angles of attack
  Helps flow re-attach after post stalled conditions
Results:
  Airplanes would require less fuel to fly the same distance
  An increased flight envelope
Standard flow at moderate angle of attack:
Flow with synthetic jet at moderate angle of attack:
https://www.youtube.com/watch?v=IytDva1y09E&feature=youtu.be

## Slide 4: Current Research at Embry-Riddle – Overview:
Objective: test current hypotheses
  1: Generating an optimized Synthetic Jet Flow will result in a re-attached
  boundary layer in posed stalled conditions
  2: Synthetic Jet flow will reduce boundary layer height in attached flow
  conditions
  3: There exists a parameter space (set of flight conditions) that will optimize
  the results of synthetic jet flow

## Slide 5: Current Research at Embry-Riddle – Methods:
Currently use CFD to model synthetic jet flow
In house made software written in FORTRAN95
  Uses a Direct Navier-Stokes solver with a forward time, central space solving scheme
  Geometry is fixed to a NACCA 0012
Current software allows the user to:
  Specify mesh size and spacing
  Reynolds Number
  Angle of attack
  Boundary conditions
  Synthetic jet strength and location

## Slide 6: Research Limitations – The Problem:
Models that are needed to effectively test the hypotheses need to be scaled up compared to previous models
  In terms of both Reynolds number and mesh size
  Allow more detail to be shown in boundary layer-jet interaction
  Allow the study of larger wings (Such as a Boeing 747)
The problem: current software cannot effectively scale current models to test larger wings or more detailed problems
  Result of time it takes to run on large meshes or at high Reynolds numbers
  Result of computational complexity

## Slide 7: Research Limitations – Complexity:
For Example:
  A mesh the research group considers large is 800 X 1600
    Number of nodes = 1.28 million
    Number of time steps = 1.2 million
    Average iterations to converge per time step = 4
    Calculations = 6.14 X 1012
    Computation time = 1.5 days
  The example mesh of realistic quality is 4.5 million nodes
Example Mesh:

## Slide 8: Research Limitations – Complexity:
Clearly moving up the complexity of the problem leads to unrealistic time to collect data – So what do we do?
We define a quantity known as the “Residual”
  LHS – RHS = 0
  Result gives us the error within the calculation at that point between each time step
We are held back from using a courser mesh for a problem because of the errors that are associated with it
  Lead to inaccurate or flat out wrong results

## Slide 9: Current Project – Beginning Investigation:
I wanted to simply plot the residuals to see where they were
Residuals migrate to the right
Appear directly above the leading edge of airfoil
Beginning question: What if they could be contained?
Residual Field for 200 X 400 model:

## Slide 10: Solution
Write an add on (new sub-routines) to the existing code
  eliminate, or reduce the residuals within models
  Allows them to be scaled as desired

## Slide 11: Current Project – Code Development Part 1:
First subroutine searches for the highest residual value
Draws a box around the region to user specified dimensions
Activates after user specified time steps

## Slide 12: Current Project – Code Development Part 2:
Subroutine two increases mesh density within the region
Leads to high precision calculation within region
Eliminates residual between time steps
Original Mesh
Refined Mesh
Note:
Blue Nodes: Original, contain original values
Black Nodes: Re-Meshed nodes
Edge nodes are weighted average of adjacent values
Interior initially calculated by solver

## Slide 13: Current Project – Code Development Part 3:
The next subroutines run values through the DNS solver
  Each routine is defined for the new mesh size
  The solver calculates to a user defined tolerance within this configuration

## Slide 14: Current Project – Code Development Part 4:
Last subroutine places processed data into main program
  Does this with respect to original position
Program then continues to compute the result
Result of Refined mesh
Region within Main Program

## Slide 15: Progress:
This is an ongoing project:
  Each subroutine within the new code has been added
  Debugging is current stage of development

## Slide 16: Next Steps:
Finish debugging the code
Run trial runs with the new code VS. original
  Done to validate code
Use the new version of the code to test hypotheses

## Slide 17: Project Goals:
Reduce the time required to compute the needed data
Enable the ability to acquire higher quality data within a timely manor
  Both goals to be met on student’s personal computers

## Slide 18: Questions?