## Slide 2: EagleSat’s Electronic Power Subsystem
Jon Lowe

## Slide 3: Electronic Power Subsystem (EPS) Outline
Requirements
EPS Description
Power Flow
Solar Cells/Panels
EPS components
Energy Budget

## Slide 4: EPS Requirements
Launch Power Activity | No electronics active during launch
Deployment Switch | Deployment switch on standoff rail disconnects all power while depressed
Access Port Locations | All connectors located in designated areas
Remove Before Flight Pin | Will have a remove before flight pin
EPS | EPS will manage all power distribution
Solar Panels | Solar panels will provide sufficient power to fulfill EagleSat’s power need

## Slide 5: EPS Description
    Collects power for EagleSat using solar panels
    Super capacitors store energy
    Vcc Batt powers Radio, Regulator
    Regulator powers Vcc Sys
    Vcc Sys powers OBC, Temperature sensors, Modem, GPS
    OBC determines standby/off

## Slide 6: Power Flow
Solar Panels
Super Capacitors
VCC BATT
Voltage Regulator
Radio
VCC SYS
OBC
Modem
GPS
Temperature Sensors

## Slide 7: Solar Cells
TriSolX Solar Wings
  28% Efficient InGaP/GaAs/Ge Triple Junction Solar Cells: Type- T01
  Voltage (Open circuit) 2.62 V
  Voltage (Max Power) 2.33 V
  Current (Max Power) 14.6 mA
  Power (Max Power) 34 mW
  Dimensions: 26.3mm x 10mm

## Slide 8: Solar Panels
Side Panels ( Top Panel (-Z) Front Panel (+X)

## Slide 9: Supercapacitors
Eaton HV1030-2R7106-R 10F (3V)
Supercapacitors
UL Listing: BBBG2.MH46887
5 per series bank (15V)
2 banks in parallel providing 4F
1125J total charge at max power

## Slide 10: Deployment Switches
3 Total switches
2 on standoff rails
1 remove before flight pin
Power disconnected when switches depressed and
remove before flight pin present

## Slide 11: Voltage Regulator
RECOM R-78E3.3-0.5
Input Range: 4V-28V
Output Voltage: 3.3V
Output Current: 500mA

## Slide 12: Temperature Sensor
Microchip TC1047A
Input Voltage 2.5V to 5.5V, 7V absolute max
Temperature Range: -40 to 125
Output Voltage: 0.1V to 1.75V

## Slide 13: Temperature Sensor
Vout = (10mV/)(Temperature ) + 500mV

## Slide 14: Cumulative Energy Budget

## Slide 15: Cumulative Energy Budget

## Slide 16: EPS Summary
All requirements are met
No electronics shall be active at launch
Deployment switches prevent EagleSat from being powered when switches are depressed
Access ports are present and allow access to connectors while in P-POD
RBF pin prevents EagleSat from being powered until removed
EPS manages EagleSat’s power distribution
Solar Panels provide sufficient power for EagleSat to function properly

## Slide 17: Questions?

## Slide 18: Backup Slides

## Slide 19: EPS Board Schematic

## Slide 20: Temperature Sensor Schematic

## Slide 21: Remaining Solar Panels
Back
Panel
(-X)
Bottom
Panel
(+Z)

## Slide 22: Perfect Energy Budget

## Slide 23: Worst Case Scenario Energy Budget