## Slide 1: GCC ASCEND
Frank Islas
Miranda Erpelding
Jonathan Wulff
Edwin Guerrero
Nersa Elya
Kennidi Ortega

## Slide 2: Introduction
Desired goals for Payload:
Make a 3D printed payload
Use satellite communication to receive live data
Gather sensor data as the payload ascends
Record burst of balloon and take 360° footage
Sound experiment

## Slide 3: Payload Design SolidWorks
Final features:
Screw holes
Lens holes
Doors
Slots for components

## Slide 4: Prototypes
Number of prototypes
Mistakes
Lessons
Testing

## Slide 5: Payload Design: 3D printing

## Slide 6: Payload Design: Populating

## Slide 7: Microprocessor
Arduino MEGA 2560
ATmega2560 chip
54 digital I/O pins , 16 analog inputs
Compact and Lightweight
4 (universal asynchronous receiver-transmitter) UARTs
C/C++ languages

## Slide 8: Coding
Arduino programmed to collect, store, and process data
Sent control signals to Hack HD Camera to turn on and begin recording
Data collected was stored on a microSD card
Data also transmitted every two minutes via a ROCKBLOCK modem
Data was received during the flight through email and was accessible around the world

## Slide 9: RockBLOCK Device:
Iridium Satellite Communication
HAM Radio vs. GCC
No license required
Cost of RockBlock: $250
10 cents for up to 50 bytes
$14 per active month
Supercapacitor
Ability to receive live data from our sensors, battery, and GPS
Arduino software designed to keep each data transmission under 50 bytes
RockBlock was controlled by Arduino, which attempted to send data every 2 minutes

## Slide 10: RockBLOCK Device:

## Slide 11: Components of Payload

## Slide 12
System Block Diagram

## Slide 13: Camera Objectives
Goals for payload Cameras:
Monitor balloon’s expansion and capturing the burst.
  Hack HD camera was used to meet this objective.
Record 360° panoramic view from the balloon payload.
  360fly camera was used to meet this objective.

## Slide 14: Hack-HD
Resolution: 1080p HD
Frame Rate: 30 FPS (Frames per Second)
Storage: External microSD Card
Controlled via Arduino

## Slide 16: 360fly
Weight: 142 g
Resolution: 1504*1504 pixels
Recording Rate: 20 Mbps
Powersource: 1630 mAh Li-polymer Battery
Record time: 2 hr with 14 hr standby
Cost: $115

## Slide 17: GPS GCC Coordinates

## Slide 18: GPS ANSR Coordinates

## Slide 19: Altitude ANSR Coordinates

## Slide 20: GPS Combined Coordinates

## Slide 21: GPS Combined Coordinates: Top View

## Slide 22: GPS: Error Distance Apart

## Slide 23: Internal Temperature

## Slide 24: Internal Pressure

## Slide 25: Internal Pressure
Launch to Burst
(Ascending)
Burst to Landing
(Descending)

## Slide 26: Humidity
Internal Temp vs. Time
Notes: Describe why humidity is so high when it is around 80,000ft
Look into seeing how the sensor works

## Slide 27: Altitude
Notes: Time was based on the built in timer in the sensor
Cut out a little before 26,000 meters or 80,000 feet
Compare to ANSR data

## Slide 28: Voltage, Current, Power

## Slide 29: UV light
UV light is measured in microwatts of ultraviolet radiation per lumen of visible light (μW/l)

## Slide 30: Sound Test

## Slide 31: Conclusion
Issues:
360fly
  Did not record properly
External Temperature
  Analog sensor did not work
UV light
  Unknown spikes in data

## Slide 32: Conclusion (con’t.)
Successes:
Made a 3D printed payload
Used satellite communication to receive live data during flight
Gathered sensor data throughout flight
Videoed burst of balloon
Sound experiment verified sound transmission throughout flight

## Slide 33: Future Plans
Use a Second RockBlock modem to have communication between the van and the payload
Using a second Arduino for transmission only
Create set of instructions for:
  RockBlock Modem
  360Fly Camera
  3D printed payload using SolidWorks

## Slide 34: Special Thanks
ANSR Team
Susan Brew
Dr. Tim Frank
Rick Sparber
William Stein