## Slide 1: Using satellite soil-moisture measurements to correct measurements of groundwater-storage change
Georgia Ross
Northern Arizona University
Dr. Jeffrey Kennedy
USGS

## Slide 2: Introduction
Groundwater is an important resource….
USGS measures groundwater-storage changes in Arizona using ground-based gravity measurements
Because gravity measures all water in the subsurface, it is helpful to remove near-surface (soil moisture) changes from deeper (aquifer) changes
NASA SMAP (Soil Moisture Active Passive) Satellite data were used to correct gravity data for soil moisture changes

## Slide 3: Measuring ground-water storage change with gravity
Changes in the amount of groundwater stored in underground aquifers are measured using ground-based gravity measurements
Changes in near-surface soil moisture create “noise” in the data and mask deeper aquifer changes.

## Slide 4: Data – gravity data
Gravity is measured using an “absolute” gravity meter that measures the acceleration of a falling mass.
Gravity measurements are made three times per year

## Slide 5: Data – Satellite Soil moisture data
SMAP….
SMAP only goes back to 2015, so we had to extend the record to 2009 using ASCAT
Soil moisture is not a direct measurement, it requires other models to account for vegetation, etc….
AirMoss…
PLOT FROM EXCEL

## Slide 6: Study Area
Flagstaff
Verde Valley
Ash Fork

## Slide 7: Analysis
Code in MATLAB applies Newton’s law of gravitation to grid-cell density changes that are caused by soil moisture.
Grid-cell elevations are obtained from the USGS National Elevation Dataset.

## Slide 8: Conclusions
Plots showing raw vs. corrected gravity time series
Chart: 1. B-15-03 11DDB
| 40753 | 40941 | 41170 | 41228 | 41367 | 41577 | 41696 | 41857 | 42017 | 42515 | 42795 | 42909 | 43025
Corrected gravity | -0.31848 | -6.3439 | -26.5053 | -21.6493 | -20.9154 | -19.2931 | -16.3008 | -19.5077 | -9.3523 | -13.1701 | -15.067 | -22.6413 | -19.281
Uncorrected gravity | 0 | -6.24 | -24.47 | -21.76 | -21.67 | -18.76 | -17.27 | -18.76 | -8.39 | -14.22 | -14.03 | -25.02 | -21.7
Depth to water | 64.5 | 66.6 | 69 | 70.9 | 72.1 | 74 | 71.2 | 74 | 76.8 | 78.4 | 80 | 79.1 | 78.6 | 79.9 | 81.8 | 81.7 | 81.5 | 82.4 | 83.7

## Slide 9: Acknowledgements
Jeff Kennedy
Research Hydrologist
USGS Arizona Water Science Center, Flagstaff
Kathleen Stigmon Sr. Program Coordinator NAU NASA Space Grant & REU
Nadine G. Barlow, PhD
Professor and Department Chair
Director, NAU/NASA Space Grant Program
Associate Director, AZ Space Grant Consortium
Department of Physics and Astronomy