## Slide 1
EagleSat 2: Design Development Lauren Barthenheier Dr. Gary Yale, Embry-Riddle Aeronautical University Arizona Space Grant Consortium Symposium April 14, 2018

## Slide 2: Outline
Background
Payload Development Testing
  Procedures
  Testing Results and Conclusions
Further Testing

## Slide 3: Background: Design Requirements
Fly two payloads
  Charged particle detector
    Catalog and record cosmic rays
  Memory degradation experiment (MDE)
    Test bit-flip corruption rates for commercially available RAM

## Slide 4: Background: MDE Mission
Detect bit flipping and memory degradation caused by solar radiation
Commercially available, consumer grade memory
  Flash
  SRAM – Static Random Access Memory (RAM)
  FRAM – Ferroelectric RAM
  MRAM – Magnetic RAM
  EEPROM – Electrically Erasable Programmable Read-Only Memory

## Slide 5: Background: MDE Main Algorithm

## Slide 6: Plugs-In Test
Purpose:
  Ensure MDE runs with constant power and data for at least 30 minutes
  Demonstrate MDE memory responds to all input commands and finds all the correct pre-seeded errors

## Slide 7: Pass / Fail Criteria
Pass/Fail | Pass Criteria | Fail Criteria
The MDE memory responds to all the command in accordance with the datasheets and timing. * If this criteria is meet, the test passes for all subsequent criteria | Responds to the commands | Does not respond to the commands
Find the correct errors. | Finds the correct number of errors | Does not find the correct number of errors

## Slide 8: Procedures
Ground payload board to static mat
Connect circuit board to power and TM4C LaunchPad
Connect TM4C LaunchPad to computer via Putty software
Press “i” key → Begin error checking for one, 15 minute cycle
Remove pre-seeded error → Repeat step 4 for 10 seconds

## Slide 9: Plugs-In Test Set-Up
MDE Board
TM4C
Power Supply
Static mat

## Slide 10: Results
Auto mode, 15 minute delay, seeded errors.
AUTO MODE. Hit M to exit.
Timer wakeup. Checking for errors...
Printing errors...
Error: 1048584
Error: 1048585
Error: 1048587
Error: 1491128
Error: 1491130
Error: 1491131
Error: 1491133
Pre-Seeded Errors
Successfully found 75 pre-seeded errors
Auto mode, 10 second delay, no seeded errors.
AUTO MODE. Hit M to exit.
Timer wakeup. Checking for errors...
Printing errors...
Sequence written, beginning next cycle.
Timer wakeup. Checking for errors...
Printing errors...
No Seeded Errors
Successfully found 0 errors

## Slide 11: Results
Pass/Fail | Pass Criteria | Fail Criteria
The MDE memory responds to all the command in accordance with the datasheets and timing. * If this criteria is meet, the test passes for all subsequent criteria | Responds to the commands | Does not respond to the commands
Find the correct errors. | Finds the correct number of errors | Does not find the correct number of errors

## Slide 12: Further Development Test
Plugs-In Test for charged particle detector
Plugs-Out Test for charged particle detector and MDE
High altitude balloon for charged particle detector and MDE

## Slide 13: Acknowledgements
Dr. Gary Yale, Embry-Riddle Aeronautical University
TeamXC, NASA Jet Propulsion Laboratory
Travis Imken, NASA Jest Propulsion Laboratory

## Slide 14
Thank You