## Slide 1
EagleSat 2: Implementation of Improved Communications Systems on UHF Steven Buck Dr. Gary Yale, Embry-Riddle Aeronautical University Arizona Space Grant Consortium Symposium April 14, 2018

## Slide 2: Outline
EagleSat-1 communications
Reason for improvement
Transceiver improvement
Antenna improvements
Additional improvements
EagleSat-2 communications
Ground station improvements
Results

## Slide 3: EagleSat-1 Communications
437.645 MHz
0.5 W transmit power
9600 baud AX.25
Monopole .87 dBi gain

## Slide 4: Reason for Improvement
Expected 30 Mb of data per pass
Each pass approximately 7 minutes
Needs more reliability and robustness

## Slide 5: Transceiver Improvement
Endurosat UHF transceiver
1 W transmit power
Specified 100 kbps over air data rate
Cost $7000

## Slide 6: Antenna Improvements
Dual antenna system
Directional antenna for data downlink
Monopole for backup communications

## Slide 7: Additional Improvements
A method to switch antenna to prevent interference
  Using an GAAS MMIC SPDT switch designed for RF signals
A method to assist with antenna pointing
  Using the AD8307 Logarithmic Amplifier

## Slide 8: EagleSat-2 Communications
UHF frequencies
1 W transmit power
Max 100 kbps using AX.25
Monopole antenna with .87 dBi gain
Directional antenna with approximately 6 dBi gain

## Slide 9: Ground Station Improvements
4.5m mesh dish antenna
Wide bandwidth transceiver

## Slide 10: Results
Preliminary switching tests are promising
Signal strength output voltage changes with received power
Eb/No, S/N have 17.1dB at horizon

## Slide 11: Acknowledgements
Dr. Gary Yale, Embry-Riddle Aeronautical University
TeamXC, NASA Jet Propulsion Laboratory
Travis Imken, NASA Jest Propulsion Laboratory

## Slide 12
Thank You