## Slide 1: Computational Fluid Dynamics (CFD) Research Project
Luke Peterson
Aerospace Engineering
Embry-Riddle Aeronautical University

## Slide 2: Background
Issues of convergence time (cost)
Precision vs speed
Extending the reach of DNS
Cost scales at least as Re2
  But the areas of high residual are highly localized.

## Slide 3: Our Problem
High Residuals
  High spatial velocity gradients (i.e. ).
Clearly, decreasing dx (increasing density in that direction) with help resolve residuals.
  Don’t want significant increase in computational cost or model complexity

## Slide 4: Common CFD Approaches
Increase uniform mesh density (N2 ≥ Re)
  High computational cost
[1]
[1]

## Slide 5: Common CFD Approaches
Biased/Skewed mesh density
  Higher model complexity
  Fewer grid points
  More arithmetic operations per point
  Increased memory lookups
[2]

## Slide 6: Common CFD Approaches
Multi-grid
  Overall fewer points  lower computational cost
  Increased model complexity and memory I/O cost
[1]

## Slide 7: Common CFD Approaches
Unstructured grid
  Highly capable for non-uniform geometry
  Very costly in
    Model complexity
    Memory
    Computation
[3]

## Slide 8: Our Solution
Higher-density, dynamic-mesh around residuals
  Increased resolution only around localized area of high residuals
    Global mesh doesn’t see additional points
  Minimal change in computational cost
  Minimal increase in model complexity

## Slide 9: Our Solution
Residual field of x-velocity

## Slide 10: Our Solution
High residuals (O~10-5) restricted to a small area of the domain

## Slide 11: Our Solution
Increase the resolution only around localized area of high residuals

## Slide 12: Results
With minimum inflation factor (2), resolution more than doubled
  Follows exponential increase in resolution with inflation factor
Computational time minimally increased (< 1%)
  Total number of points in subdomain are fewer than global domain.
  However, if equal or even larger, the subdomain only runs a single iteration before being copied back to the global mesh for continuation of simulation.

## Slide 13: Results
X-velocity contour plot (201x401 or 80,601 nodes)

## Slide 14: Results
X-velocity contour plot with subdomain identified.

## Slide 15: Results
Global x-velocity subdomain (260 nodes or 0.32% of global mesh)

## Slide 16: Results
Mesh-refine domain (inflation factor = 2  4x nodes, 1,107 nodes or 1.4% of global mesh)

## Slide 17: Results
Mesh-refine domain (inflation factor = 4  16x nodes, 4,293 nodes or 5.3% of global mesh)

## Slide 18: Results
Optimization still remains

## Slide 19: Final Goal
[4]

## Slide 20: References
[1] https://www.mathworks.com/matlabcentral/answers/378693-how-to-create-a-non-uniform-2d-grid
[2]https://cubit.sandia.gov/public/14.0/help_manual/WebHelp/mesh_generation/adaptivity_and_sizing_functions/bias_sizing_function.htm
[3] http://ta.twi.tudelft.nl/users/wesselin/projects/unstructured.html
[4] https://www.youtube.com/watch?v=IytDva1y09E

## Slide 21: Questions