## Slide 1: Uses for LWIR and LiDAR Sensor Fusion in Relation to sUAS Detection
Jonathan M. Buchholz
Iacopo Gentilini

## Slide 2: Introduction
Rise of small Unmanned Aerial System (sUAS)
NASA’s UAS Traffic Management (UTM)
Methods require sensing capabilities
  Detection
  Location
  Categorization
Long Wave InfraRed (LWIR)
Light Detection and Ranging (LiDAR)
Sensor fusion
(freeflysystems.com/alta-6/specs)

## Slide 3: Methodology
Research sensor fusion methods
General fusion
LiDAR and visible
for reference
Perform trade study of available sensors
Performance
Cost
Weight
Design sensor mount
CATIA
3D printed
Choose processor
Raspberry Pi 3
  Small
  Simple
Arrange data capture method
GPIO trigger for LWIR
ROS packages for LiDAR
Develop sensor fusion algorithm
Geometric
transformations
Pixel-level correlation

## Slide 4: Sensors and Specifications
FLIR® VUETM Pro
LWIR Camera
7.5 - 13.5 µm wavelength
336x256 resolution
35° HFOV, 27° VFOV
30 FPS
Velodyne® PuckTM LITE
LiDAR Scanner
903 nm wavelength
360° HFOV, 30° VFOV
100m effective range, ±3cm
~300,000 points per second
(www.FlirMedia.com)
(www.VelodyneLiDAR.com)

## Slide 5: Sensor Fusion Algorithm
Geometric transformations
Pixel-level color correlation

## Slide 6: Conclusion
Sensor fusion advantages:
  LWIR contrast
  LiDAR depth
  Independent of visible spectrum
Machine Learning (ML) Compatibility
  Fused data for training neural networks
  Recognition in addition to detection and localization
Use on sUAS
  Lightweight design
(Siewert, 2013)

## Slide 7: Challenges
Mostly software-based:
Linux environment
ROS architecture
BASH scripting
Python
(www.Python.org)
(www.ROS.org)

## Slide 8: Future Work
Capture data from sUAS platform
Adapt fusion algorithm to RTOS
Compile data for ML functionality
Python & Bash
Guaranteed data sync
ALTA 6
Preliminary flight data
C, C++ conversion
Refinement of algorithm
Explore DAA methods
Publish data sets
Prepare automated data capture

## Slide 9: The Larger Picture
Drone Net
ERAU Prescott & CU Boulder
Graduate and undergraduate
Detection, localization, classification of sUAS in Class G airspace
Challenging effectiveness of RADAR
  Reliability
  Cost
(Siewert, 2018)

## Slide 10: Acknowledgements
Dr. Iacopo Gentilini
Dr. Sam Siewert
Dr. Anne Boettcher
Dr. Jonathan Gallimore
Jim Weber

## Slide 11: Questions?
Please contact: Jonathan M. Buchholz buchholj@my.erau.edu

## Slide 12: Thank You