## Slide 1: Empirical noise distribution models for high contrast direct imaging
Dominic Sanchez
University of Arizona, Undergraduate
Mentor: Dr. Jordan Stone

## Slide 2: Background
Adaptive optics (AO) is a technology that measures and corrects wavefront errors
Restores image quality by correcting errors caused by the atmosphere
Wavefront error correction allows for higher resolution
Necessary for exoplanet direct imaging

## Slide 3: Directing Imaging
Starlight illuminates planets which allows for direct imaging
Yields information about exoplanet orbit, size, temperature, surface properties etc.
Difficult:
  Planets are dim
  Noise can “wash out” planet signal
Credit: Hatzes et al., 2003

## Slide 4: Noise
Photon noise
  Random fluctuation of photons
Speckle Noise
  Random irradiance pattern from mutual interference
Difficult to discern exoplanet signals
Coronagraph used to limit photon noise in some systems
Exoplanet?
Credit: D. Defrère, O. Absil, P. Hinz, J. Kuhn, D. Mawet, et al.

## Slide 5: Distribution Models
Noise distributions used for exoplanet confirmation
  Confidence level (CL)
CLs are found using Gaussian distribution
Quasi-static speckle noise
  Modified Rician (MR)
Noise distribution modeling necessary to avoid false positive detections
Noise is averaged and subtracted out
Credit: J.Stone

## Slide 6: Empirical Model
Create model for future exoplanet confirmation
  CL calculations
Gather annular data from LBTI database
  Two mirrors
  Timespan: 2013-2017
Distribution may or may not be Gaussian
  Verify residual distribution

## Slide 7: Results
Probability Density Function (PDF)
Cumulative Density Function (CDF)
  Compare empirical with Gaussian CDF
Models illustrate non-Gaussian
Can be used for future exoplanet detection
Differences in data can also yield useful information
R=20
R=60
R=100
R=150

## Slide 8: Results
Probability Density Function (PDF)
Cumulative Density Function (CDF)
  Compare empirical with Gaussian CDF
Models illustrate non-Gaussian
Can be used for future exoplanet detection
Differences in data can also yield useful information
R=20
R=60
R=100
R=150

## Slide 9: Acknowledgements
I would like to thank the UA/ NASA Space Grant Consortium making this experience possible.
I would like to especially thank my mentor Dr. Jordan Stone for all of the support.

## Slide 10: References
Defrère, D., Absil, O., Hinz, P., Kuhn, J., Mawet, D., Mennesson, B., … J, S. (2014). L’-band AGPM vector vortex coronagraph’s first light on LBTI/LMIRCam. Adaptive Optics Systems IV, 9148, 91483X. https://doi.org/10.1117/12.2057205
Jensen-Clem, R., Mawet, D., Gonzalez, C. A. G., Absil, O., Belikov, R., Currie, T., … Tanner, A. (2017). A New Standard for Assessing the Performance of High Contrast Imaging Systems. The Astronomical Journal, 155(1), 19. https://doi.org/10.3847/1538-3881/aa97e4
Marois, C., Lafreniere, D., Macintosh, B., & Doyon, R. (2008). Confidence Level and Sensitivity Limits in High Contrast Imaging. The Astrophysical Journal, 673(1), 647–656. https://doi.org/10.1086/523839
Mawet, D., Milli, J., Wahhaj, Z., Pelat, D., Absil, O., Delacroix, C., … Pueyo, L. (2014). Fundamental limitations of high contrast imaging set by small sample statistics. The Astrophysical Journal, 792(2), 97. https://doi.org/10.1088/0004-637X/792/2/97