## Slide 1: Schlieren Optical Visualization
Victor Padilla
Dr. Alex Craig, Dr. Lutz Taubert, John Flood
4/13/2019

## Slide 2: University of Arizona BLST
Boundary-Layer Stability and Transition Laboratory
  Research concerning laminar-turbulent transition in fluid flow
  Mach 4 Ludwieg Tube Wind Tunnel
    100 ms run time
    Quiet flow below 14.5 psi
    Pressure Transducers
    Automated
  Mach 5 Ludwieg Tube
    100 ms run time
    Quiet flow below 200 psi
    Pressure Transducers

## Slide 3: What is Schlieren?
Visual Method of observing density changes in fluids using optics
Conventional Setup
  Camera
  Monochromatic Point Source for Light
    Less scattering/blurriness/diffraction
    Resolves possible aberration issue
  Lens/Mirrors
    Focusing/Filtering
  Knife Edge
    Controls light intensity
    Increases contrast
    Blocks certain optical paths of light
Density changes are the driving aspect of projections
  Density changes of fluids change light intensity

## Slide 4: How Schlieren Works
Refractive Index changes
  Refractive index dependent on fluid/medium density
  Velocity of light waves change
Spatial Filtering
  Knife Edge
  Lens
  Mirrors

## Slide 5: Why Is It Important?
Detection and Visualization
  Empirical visual evidence
  Shows changes in Temperature, Pressure, and Density
Image Processing
  Image processing generates quantifiable results

## Slide 6: Focusing Schlieren
Checkered Grid Display
    Grid lines are opaque and transparent
      Act as knife edge
Monochromatic Broad Light Source
    Shines behind grid toward camera
Focusing
    Camera focuses on light from grid
      Grid focusing absolves initial unwanted refractive indices

## Slide 7: Schlieren Image Examples

## Slide 8: Summary
Schlieren Imaging
  Method to view density changes in a fluid
Density Changes
  Temperature and Pressure changes/effects
  Refractive Indices
    Different light wave velocities in separate mediums