## Slide 1
Using Fluorescence Tools in the Field and in the Lab to Understand Tempe Town Lake’s Biogeochemical Cycles
Elinor Sauer and Dr. Hilairy Hartnett
School of Earth and Space Exploration

## Slide 2: Introduction Tempe Town Lake (TTL)
The Hartnett lab has monitored TTL water chemistry and dissolved carbon since 2005
For the past year, I have sampled TTL twice a week
A new DataSONDE has also been collecting in situ data for one year
My project compares lab results with in situ data from the SONDE
Things I Measure:
pH
Dissolved Oxygen
Conductivity
Dissolved Organic Carbon
UV and Fluorescence
A filtered TTL sample ready for fluorescence analysis
Elinor Sauer and Dr. Hartnett gathering data at TTL

## Slide 3: Background SONDE
Background Data SONDE
The SONDE measures pH, Dissolved Oxygen, Conductivity, and fluorescent Dissolved Organic Carbon
  the same parameters I measure each week
Collects data every 30 minutes
Monthly data retrieval and SONDE maintenance

## Slide 4: Background Fluorescence
Background Fluorescence
Fluorophores are molecules that can be excited by a certain wavelength and emit a longer wavelength
The difference in excitation and emission spectra can be used to distinguish different molecules within a sample
In the lab we test across the spectrum of wave lengths, producing 3D graphs
The SONDE only measures at a specific wavelength

## Slide 5: The Question
The Big Question
Is the SONDE data consistent with the lab measurements?
If they are, I expect to see something like:
If they are not, I expect differences between the lab data and the SONDE data:

## Slide 6: Methods
Methods dataSONDE/Lab comparison study
Collect samples every 30 minutes
Measure fluorescence and water chemistry
Compare with dataSONDE!

## Slide 7: Data Fluorescence from Lab
9:00 AM
9:43 AM
10:32 AM
11:00 AM
11:30 AM
12:16 PM
12:50 PM
Data Fluorescence from Lab
Fluorescent components are derived from a PARAFAC model (Cory and McKnight, 2005)
Fluorescence Intensity (relative units)

## Slide 8: Data Fluorescence from Lab
Data Comparison SONDE data and Total fluorescence
Total Fluorescence is the sum of all the intensity in the EEM
Scale is not the same, but the pattern basically is

## Slide 9: Data Fluorescence from Lab
Data Comparison SONDE data vs Individual Components
Of the thirteen components, these four had the strongest relationship to the SONDE data
R2 is still understandably small, due to the limited sample size
These may indicate both positive and negative relationships between components and SONDE data

## Slide 10: Data Fluorescence from Lab
  Total Fluorescence and SONDE CDOM patterns are consistent
      CDOM is a good proxy for fluorescent carbon
  Relationships, both positive and negative, between the SONDE and certain components are evident in the comparison
    These could have bigger implications for the applicability of the SONDE
New questions:
  Do these pattern hold true over the other parts of the day?
  Do CDOM and total Fluorescence reflect carbon concentration?
Next steps:
Do the field experiment again at different times of day
Measure total carbon concentrations using DOC
Conclusions, Implications, and Future Plans
Thank you to Josh Nye for help with the modelling, Tessa Fisher for SONDE data and Donald Glaser for sampling assistance!