## Slide 1
Crew Member Vital Signs
as Indicators of Environmental Changes aboard Space Habitats
Shaun Brown1
Mentor: Wolfgang Fink1, Ph.D., FAIMBE, FPHM, FSPIE
1Visual and Autonomous Exploration Systems Research Laboratory,
College of Engineering, University of Arizona, Tucson, AZ, USA
UA/NASA Space Grant
2020 Statewide Symposium, Tucson, AZ

## Slide 2
Acknowledgements & Disclosures
Research support:
Shaun Brown has been supported by NASA traineeship grant NNH18ZHA007C via the Arizona Space Grant Consortium
NASA SBIR Phase II grant 80NSSC1900130
Edward & Maria Keonjian Endowment at the College of Engineering, University of Arizona
This presentation is part of a paper given at the IEEE Aerospace Conference on March 12, 2020:
Brown S, Prasad A, Fink W (2020) Inventory of Vital Sign Changes as Indicators of Environmental Changes aboard Space Habitats; IEEE Aerospace Conference Proceedings, paper #2794, Big Sky, MT

## Slide 3
Motivation
NASA Relevance
NASA’s Space Technology Grand Challenges addressed
Motivation of ‘Crew as a Sensor’ Paradigm to monitor Space Habitat Health
Sensing Framework
Environmental Change Indicator Modality:
  ECG
  Blood Oxygenation (SpO2)
  Ocular Structure and Visual Performance
Study Results
Conclusions & Next Steps
Outline

## Slide 4
Expansion of human presence into low-Earth orbit
Autonomous operation of space habitats
Supplemental data to support those systems
Ensure a breathable atmosphere aboard space habitats
NASA’s goal: Lunar Gateway orbiting the Moon
Motivation

## Slide 5
NASA’s Lunar Orbital Platform Gateway
Important to ensure low-payload and self-reliance of crew-members (see also healthcare autonomy paradigm vs. tele-medicine paradigm (Popov et al., IJPHM 2019))
Autonomous operation of life support systems
Autonomous regulation of atmosphere aboard space habitats
NASA Space Technology Grand Challenges:
  Space Health and Medicine
  Space Colonization
NASA Relevance

## Slide 6
Grand Challenge:
“Eliminate or mitigate the negative effects of the space environments on human physical and behavioral health, optimize human performance in space and expand the scope of space based medical care to match terrestrial care.”
Stated Problem:
“Space is an extreme environment that is not conducive to human life. Today’s technology can only partially mitigate the effects on the physical and psychological well-being of people. In order to live and effectively work in space for an extended period of time, people require technologies that enable survival in extreme environments; countermeasures that mitigate the negative effects of space; accommodations that optimize human performance; comprehensive space-based physiological and physical health management and prompt and comprehensive medical care in a limited infrastructure.”
http://www.nasa.gov/pdf/503466main_space_tech_grand_challenges_12_02_10.pdf
NASA’s Space Technology Grand Challenges:
Space Health and Medicine

## Slide 7
Grand Challenge:
“Create self-sustaining and reliable human environments and habitats that enable the permanent colonization of space and other planetary surfaces.”
Stated Problem:
“Currently, the infrastructure and integrated technologies needed to enable permanent, self-sufficient human settlements away from Earth do not exist. Effective close-loop systems do not exist to replenish consumable resources. This makes long-term stays cost-prohibitive and poses significant risk to personnel if resupply missions do not arrive on time.”
http://www.nasa.gov/pdf/503466main_space_tech_grand_challenges_12_02_10.pdf
NASA’s Space Technology Grand Challenges:
Space Colonization

## Slide 8
Paradigm originally formulated by Andrew Hess (President PHM Society), 2019
Underlying Principle: Canary in a Coal Mine
Organisms (i.e., crew members) function as versatile biosensors
Paradigm provides greater context and more data to onboard autonomous monitoring systems
Autonomic vital sign changes, due to space habitat environmental changes, being transduced in both qualifiable and potentially quantifiable modalities:
  ECG
  Blood oxygenation (SpO2)
  Ocular structure changes
  Visual performance assessment
Motivation of ‘Crew as a Sensor’ Paradigm
To Monitor Space Habitat Health

## Slide 9
Fabricated/artificial sensors
  Individual pressure transducers (e.g., recording habitat leaks), photodiodes (e.g., recording lack of habitat light shielding), O2/CO2/CO-detectors (e.g., recording of outgassing events), thermosensors (e.g., recording of thermal shielding failure), etc.
Combinations of sensors
Multi-modal interpretation of sensor data (potential use case for Machine Learning, Deep Learning, Artificial Intelligence, etc.)
Abiotic sensors combined with human biosensors
Sensing Framework

## Slide 10
Measurable ECG changes in response to O2, CO2, CO, and radiation
Looking at effects in the morphology of ECG readings
Features of a standard ECG wave
Environmental Change Indicator Modality:
ECG

## Slide 11
Top: ECG readings before CO2 administration. Bottom: ECG readings after CO2 administration with P-wave inversion.
Top: ECG recording before radiation therapy in a 48-year-old woman. Bottom: After 6 months postoperative radiation therapy, showcasing T-wave changes.
Environmental Change Indicator Modality:
ECG: Examples of Morphology Changes

## Slide 12
Adverse Event | Environmental change | Qualitative Symptoms | Morphology response, i.e., crew member vital sign change
Fire in microgravity environment | CO increase, formaldehyde production [52] | Headache, nausea, loss of consciousness | ST-segment elevation/depression; T-wave inversion
Leak in habitat | Pressure drop, O2 decrease [53] | Shortness of breath, dizziness, visual disorders, rapid heartbeat | RS-T segment elevation, T-wave inversion
Outgassing from habitat components [54] | CO2 increase, presence of volatile compounds | Shortness of breath, dizziness, fatigue, loss of consciousness | Lowering and inversion of P-waves, T-wave inversion
Environmental Change Indicator Modality:
ECG: Morphology Shifts in Response to Adverse Events

## Slide 13
Pulse oximeters to measure arterial oxygen saturation (SpO2)
Functions to observe abnormalities in O2 and CO2 saturations (e.g., O2-leaks or CO2 outgassing)
Cannot distinguish between O2 and CO (e.g., may not detect CO-outgassing event aboard a space habitat)
Commercial-off-the-shelf (COTS) pulse oximeter
Environmental Change Indicator Modality:
Blood Oxygenation (SpO2)

## Slide 14
Smartphone-based ophthalmic examination devices (Fink et al., SPIE 2016)
Spaceflight-Associated Neuro-ocular Syndrome (SANS)
  Caused by microgravity
  Manifested as decreased near-field visual acuity
Vascular and ocular structure remodeling
  Caused by elevated CO2
  Changes manifest over time (i.e., not immediate)
  Recording of subtle drifts/shifts in environmental parameters
Example smartphone-based ophthalmic examination devices, from left to right: microscope, slit lamp, and fundoscope/ophthalmoscope (Fink et al., SPIE 2016)
Environmental Change Indicator Modality:
Ocular Structure and Visual Performance

## Slide 15: Visual Performance Assessment System (Adams, Cerwin, Fink, SPIE 2016)
Environmental Change Indicator Modality:
Ocular Structure and Visual Performance (cont.)
Tablet configuration of visual performance assessment system.
Manifestation of scotomas (i.e., visual field defects, exhibited by missing grid lines) on an Amsler grid.
CVFATM Visual performance test result: central hill-of-vision.
Potentially record visual field/visual performance defects due to radiation

## Slide 16
Environmental Change Indicator Modality | Sensitivity | Specificity | Time to Criticality
ECG | Autonomic nervous system responds to all stimuli – ECG captures autonomic nervous system changes, e.g., measures the heart | Imprecise – Individuals autonomically respond to stimuli differently and with varying degrees | During exposure; point measurements
Blood Oxygenation | Accuracy of ± 2% in measuring blood oxygen saturation | Cannot discern between O2 and CO in blood saturation readings | During exposure; point measurements
Ocular Structure and Visual Performance | No immediate changes as a result of specific atmospheric stimulus | Microgravity is primary causative factor; CO2 is a secondary factor | Long term; subtle changes over time
Study Results
Sensitivity, Specificity, and Time to Criticality of Modalities

## Slide 17
Conclusions & Next Steps
Direct ECG response non-specific to environmental changes
SpO2 good for O2, but not in the presence of CO
Ocular structure changes and visual performance may record only subtle drifts/shifts in environmental parameters over longer periods of time, hence not useable during exposure
Need to establish ECG motifs that are representative of environmental parameter changes
Subsequent anomaly detection (i.e., utilizing machine learning, deep learning, artificial intelligence)

## Slide 18
Questions?
Thank you!
For more information:
Prof. Wolfgang Fink, Ph.D.
Visual and Autonomous Exploration Systems
Research Laboratory
Depts. of Electrical & Computer Engineering, Biomedical Engineering,
Systems & Industrial Engineering, and Ophthalmology & Vision Science
University of Arizona
wfink@email.arizona.edu
http://autonomy.arizona.edu