## Slide 1: Biogas Production from Microalgae following Freeze-Heat Pretreatment
Galen Dennis
Advisor: Dr. Terry Baxter – NAU College of College of Engineering, Informatics, and Applied Sciences
Arizona Space Grant Consortium Symposium
17 April 2021

## Slide 2: Purpose and Applications
Relevance
Biosystems are effective for gas and nutrient recycling
Long-distance space travel requires efficient recycling systems
Project Question
Preheating increases anaerobic digestion efficiency, does pre-cooling have any noticeable effects?
  Based on the observation that frozen algae samples are much less viscous after defrosting.
Interior 25 0C
Exhaust Heat > 25 0C
Incubator
Anaerobic Digesters
System diagram for growing algae in a space vessel
Vacuum < -100 0C
Fuel
CO2
Nutrients
Oxygen
Biomass

## Slide 3: Experimental Methods
Algae Bioreactor Raceway
400 mL Anaerobic Digesters
CO2 Scrubber
Pretreatment Approach | Potential Treatments
Hot | Heating (70 0C), boiling (100 0C), autoclaving (120 0C)
Cold | Freezing (0 0C), Below Freezing (-40 0C), liquid nitrogen (-196 0C)
Cycles | Boil-Freeze, Liquid Nitrogen-Autoclave… etc.
300 mg/L
15000-30000 mg/L
Biomass
Biogas
Concentration
3-7 days of production

## Slide 4: Results
Heat-treated (left) and untreated (right) algae
Assumptions
10 % of biomass is retained by digesters
The product biogas is pure methane
Digesters will have the same relative response to the same feed
Chart: Digester A Production Rate
No Algae | 1.3064 | 0.49269
Untreated Algae | 1.7622
70 Degree Heat | 3.3791
Boiling Heat | 3.4006
Autoclave | 2.8748
Chart: Digester B Production Rate
No Algae | 2.7847
Untreated Algae | 3.9372
Untreated Algae | 5.8028
Untreated Algae | 5.3616
Untreated Algae | 4.8791

## Slide 5: Results
Chart: Pretreated and Control Biogas Composition
| %CO2 -A | %CH4 - A | %CO2 - B | %CH4 - B
Butyrate | 0.10473 | 0.89527 | 0.098571 | 0.90143
Untreated | 0.11708 | 0.88292 | 0.16257 | 0.83743
70C heat | 0.14934 | 0.85066 | 0.18656 | 0.81344
Boiling | 0.16295 | 0.83705 | 0.1952 | 0.8048
Autoclaved | 0.16152 | 0.83848 | 0.19353 | 0.80647
Chart: Digester Biogas Production Relative to Na-Butyrate only Diet
| Butyric Only | Untreated Algae | 70 Degree Heat | Boiling Heat | Autoclave
Digester A | 1 | 1.3489 | 2.5865 | 2.603 | 2.2006
Digester B | 1 | 1.4138 | 2.0838 | 1.9254 | 1.7521

## Slide 6
Heat pretreatment led to improved overall gas production, and methane content
Improvements
  Maintain pH
  Standard testing lengths
  Multiple test and control digesters
Chart: Digester pH Over Time
| 44137 | 44142 | 44146 | 44153 | 44159 | 44172 | 44179 | 44186 | 44193 | 44200 | 44207 | 44214 | 44221 | 44228 | 44232 | 44235 | 44239 | 44242 | 44246 | 44250 | 44253
A | 7.07 | 6.84 | 6.9 | 7.03 | 7.19 | 7.37 | 7.31 | 7.24 | 7.22 | 7.15 | 7.35 | 7.29 | 7.11 | 7.19 | 7.08 | 7.1 | 7.09 | 7.01 | 7.03 | 7 | 6.98
B | 7.3 | 7.22 | 7.45 | 8.02 | 8.03 | 7.8 | 7.79 | 7.64 | 7.52 | 7.53 | 7.67 | 7.72 | 7.52 | 7.65 | 7.48 | 7.58 | 7.55 | 7.45 | 7.43 | 7.33 | 7.41
Conclusions
What’s left
  Cold pretreatment
  Cold-hot cycles
  Hot-cold cycles

## Slide 7
Acknowledgments
Dr. Terry Baxter
NAU Environmental and Civil Engineering Department - Biotechnology Lab
NAU NASA Space Grant Internship
Arizona Space Grant Consortium
Thank you