## Slide 1: The Contribution of Plants and Pollution to Tucson’s Urban Ozone Problem
Richard Pepel
(department of Chemical and environmental engineering)
Mentor: Dr. Eric Betterton
(department of hydrology and atmospheric sciences)

## Slide 2: Background
  In 2018, ozone levels in Tucson exceeded the Environmental Protection Agency’s national air quality standards (70 ppb) for the first time
  Ground-level ozone is a respiratory health risk and an environmental hazard
  The recipe for ozone production is:
            Volatile Organic Compounds (VOCs) + Nitrogen oxides (NOx) + Sunlight  Ozone
  Tucson’s VOC profile was unknown prior to this project
  The goal of this project is to determine the following in Tucson:
          The limiting reagent (between VOCs and NOx) for ozone production
          How much of an impact VOCs from plants have on ozone production
          Whether seasonal VOC trends can be observed

## Slide 3: Procedure
  Gas Chromatography is used to determine the concentration and speciation of VOCs
  Ambient air samples are taken directly on the Physics and Atmospheric Sciences (PAS) rooftop lab at 1 or 3-hour intervals
  Summa cannisters were also used to take samples throughout Pima County
  Over 60 Summa cannister samples and over 12,000 ambient air samples have been taken
Gas Chromatograph used to analyze air samples
PAS rooftop sampler
Summa cannister

## Slide 4: Sampling Locations
Summa cannister sampling locations

## Slide 5: Anthropogenic vs. Biogenic VOCs
Chart: VOC Contribution
| 43990 | 43991 | 43992 | 43993
Alkanes ≤ 5 | 37.43 | 85.48 | 84.64 | 92.92
Alkanes ≥ 6 | 70.01 | 94.68 | 83.2 | 94.82
Alkenes | 9.85 | 19.83 | 44.95 | 23.93
Alkenes (Biogenic) | 0 | 7.95 | 0 | 8
Aromatics | 98.28 | 126.02 | 111.01 | 130.4
Total VOC | 215.57 | 333.96 | 323.8 | 350.07
NOx | 13 | 20.5 | 20.1 | 12.7
Ozone | 53 | 72 | 67 | 78

## Slide 6: VOC Concentration vs. Ozone Concentration
Chart: Daily Max VOCs vs. Ozone - Children's Park
| 43983 | 43984 | 43985 | 43986 | 43987 | 43988 | 43989 | 43990 | 43991 | 43992 | 43993 | 43994 | 43995 | 43996 | 43997 | 43998 | 43999 | 44000 | 44001 | 44002 | 44003 | 44004 | 44005 | 44006 | 44007 | 44008 | 44009 | 44010 | 44011 | 44012 | 44013 | 44014 | 44015 | 44016 | 44017 | 44018 | 44019 | 44020 | 44021 | 44022 | 44023 | 44024 | 44025 | 44026 | 44027 | 44028 | 44029 | 44030 | 44031 | 44032 | 44033 | 44034 | 44035 | 44036 | 44037 | 44038 | 44039 | 44040 | 44041 | 44042 | 44043
VOCs | 376.06 | 307.15 | 308.74 | 215.44 | 251.29 | 216.41 | 334.3 | 324.4 | 350.37 | 229.01 | 423.93 | 347.21 | 485.48 | 204.58 | 383.7 | 194.14 | 386.07 | 349.37 | 307.06 | 322.7 | 407.52 | 439.98 | 221.5 | 387.25 | 301.53 | 200.48 | 209.7 | 247.5 | 269.82 | 284.9 | 273.67 | 223.55 | 307.41 | 315.98 | 259.2 | 255.05 | 203.64 | 243.21 | 265.79 | 224.46 | 208.91 | 237.32 | 292.84 | 376.04 | 498.01 | 220.52 | 238.93 | 239.56 | 267.57 | 234.35 | 273.5 | 268.91 | 283.1 | 312.76 | 266.03

## Slide 7: Seasonal Reactivity

## Slide 8: Tucson and Phoenix – Ozone Isopleth
- Tucson
- Phoenix
(Estimate)
Chart: 

## Slide 9: Conclusions
  Plant emissions are responsible for a significant amount of VOC production, especially on days with elevated ozone levels
  The largest contributors to ozone production in Tucson are anthropogenic emissions
  Ozone production generally increases with VOC concentrations
  Total VOC reactivity varies seasonally
  Tucson appears to be NOx-limited
  Tucson NOx appears to be lower than Phoenix
  Tucson VOC appears to be comparable to Phoenix
  Further research is required to confirm these findings

## Slide 10: Thank you
Thank you to the Arizona Space Grant Consortium and to everyone involved in this project:
Michelle Coe – Arizona Space Grant Consortium
Dr. Chandra Holifield Collins – Arizona Space Grant Consortium
Dr. Eric Betterton – Department of Hydrology and Atmospheric Sciences
Kyle Rine – Department of Hydrology and Atmospheric Sciences
Kisiel Chapman – Department of Hydrology and Atmospheric Sciences
Dr. Eduardo Saez – Department of Chemical and Environmental Engineering
Ruby O’Brien-Metzger – Department of Aerospace and Mechanical Engineering
Diana Picón – Department of Biosystems Engineering

## Slide 13: NOx Concentration vs. Ozone Concentration
Chart: Daily NOx vs. Ozone - Children's Park