## Slide 1
EagleSat-II
On Board Computer (OBC) Subsystem
Katherine Rocha

## Slide 2: OBC Overview
Architecture Description
FPGA Fabric
MircoBlaze Soft Processing Core

## Slide 3: Architecture Description
Centralized computer system
Triple Mode Redundancy solution to radiation
MicroBlaze SoftCore
  Connects to all other subsystems, through FPGA Fabric
  Processes all bus system data and telemetry
  Communicates with the ground through COMMS subsystem

## Slide 4: FPGA Fabric – Overview
Ease of development for the team is critically important
FPGA with softcore to meet instrument timing requirements

## Slide 5: FPGA Fabric – Firmware
Ease of development is a priority
Software being developed by each subteam semi-independently

## Slide 6: FPGA Fabric – Additional Telemetry
Comms Packet Handling
  Packetizes data and telemetry for downlink asynchronously

## Slide 7: MicroBlaze Softcore – Overview
Interfaces with all other bus systems and payload stack
  Receives and interprets commands from the ground
Designed in house
  Custom development for mission-critical system
  Real-Time Processor Preset Configuration
  Operating System TBD
  Flight SW Framework TBD

## Slide 8: MicroBlaze – Firmware
Using Xilinx IP and example code to create the softcore
External interfaces adjusted to work with Neso Artix 7
Custom PDL with interfaces to FPGA
Off-loading processing to FPGA fabric

## Slide 9: MicroBlaze Software – Operating Modes
Detumble
  Entered at every boot, all subsystems off except OBC and ACS
  ACS detumbling the spacecraft until low rotation rate
Safe mode
  Spacecraft reduced to barebones operation
  Payloads off, COMMS attempts to establish communication with ground station
Normal operating mode
  Main science mission underway
  Payloads fully operating, ACS stationkeeping
Figure 7: EagleSat-II Operating Modes

## Slide 10: On-Board Computer – Board Design
Prototype PCB early in design/build process
  Parts and interfaces selected, early schematic designs
  Pin and peripheral assignments planned, subject to change
MDE prototype already running on TM4C
  Black box test of descaled system during high-altitude balloon flight
  Possible migration to FPGA
CRP prototype in development
  MCU + FPGA development difficult – difficult to test either until both complete
  Prototype Complete – testing being done with radiation sources

## Slide 11: Questions?