## Slide 2: SPECIAL THANKS TO
Luis Arce Gutierrez
Nicholas Stein
Dr. Tim Frank
Rick Sparber

## Slide 3: PROJECT OBJECTIVES
Demonstrate the RF skip in the atmosphere.
Gather and record CO2 and humidity readings from the atmosphere.
Examine the effects of radiation on Garden Cress Seeds.
Record the expansion of a marshmallow Peep in high altitude.

## Slide 4: System Block diagram

## Slide 5
Payload Housing

## Slide 6
Stuffed Inside payload

## Slide 7: RF Field Sensor

## Slide 8
The story of the RF Field sensor:
The RF Field sensor
First amplifier shorted out during calibration
The new OP-Amp based amplifier

## Slide 9
The Relative Field Receiver
Range: 0.1-2K MHz
Mission: Prove Skip exists!

## Slide 10: CO2 and Humidity Sensor
CO2 and humidity at higher altitudes

## Slide 11
SCD41 CO2 Sensor
Hardware
Measures C02 ppm
Gives Humidity Readings
Communicating with Arduino

## Slide 12: CO2 Sensor Issues
Notes: Flight Data Recorder accepts analogue signals, but not digital.

## Slide 13: CODES FOR CO2 SENSOR

## Slide 14
SCD41 CO2 Sensor Data
Notes: CO2 Readings drop as we increase altitude.

## Slide 15: Radiation vs Plant Seeds
The purpose of this experiment was to measure the radiation and determine the effect is had on seeds

## Slide 16: Geiger Counter
Pocket Geiger Counter from Radiation Watch
Detects Beta and Gamma Rays.
Used two different codes to run and store data to separate SD card
Calibrated and tested using a sample of radioactive material

## Slide 17: Geiger Mishap
No data Geiger counter was recorded during the flight.
The wire powering the Geiger counter disconnected from the Arduino.
Wire pin was too small for socket.

## Slide 18: Plant Seed Experiment
Garden Cress Seeds
Before launch, a batch of seeds were grown to show viability.

## Slide 19
Flight Group
Day 5 morning
Day 5 evening
Day 6 Morning
Day 6 Evening
Non-Flight
Day 5 morning
Day 5 evening
Day 6 morning
Day 6 evening

## Slide 20
Day 8 Morning
Day 11 Evening
Flight Group
Non-Flight
Day 8 Morning
Day 11 Evening

## Slide 21: Overall Growth Flight vs. Non-flight
Seeds after flight were still able to grow.
10 Samples were taken from each batch.
Measurements taken with a caliper and measured in mm.
Measurements taken on day 11.
Flight (mm) | Non-Flight (mm)
78 | 90
88 | 55
34 | 21
83 | 90
51 | 53
41 | 79
63 | 44
36 | 87
44 | 44
Average (mm) | 58.6 | 60.8
68 | 45
Notes: Flight conditions did not harm them

## Slide 22: ACCELEROMETER TEMPERATURE PRESSURE
DE-ACCM6G Buffered ±6 Accelerometer
3 TMP36 Temperature Sensors
Camera Sensor
Seed Sensor
External Sensor
ASDX Series Pressure sensor (ASDX015)
ADDITIONAL SENSORS

## Slide 23
Burst Land
Camera
Seeds
Outside

## Slide 24: Camera
Runcam 2
Records 1080p 60 FPS
Recorded launch, through burst, then stopped
Memory card was full
We forgot to erase 24 hours of test footage

## Slide 26: QUESTIONS?
Jose ocampo
GenARO Rivera
Shelby Bump
Rik Bloemers

## Slide 27
https://rik2049707.wixsite.com/ascend
Visit our website!
< SCAN ME!