## Slide 1: An Apparatus for the Experimental Simulation of the Effects of Wind Transport on Martian Sands
Evolution | Testing | Use-case
Mentors: Dr. Devon Burr2, Anna Baker2
Rachel Fry1
Northern Arizona University
1Applied Physics and Materials Science
2Department of Astronomy and Planetary Science

## Slide 2: Background
Global trends in bed-form mobility (Chojnacki et al. 2019)
NASA/JPL-Caltech/UofA, 2009
Sand
Widespread on Mars
Movement driven by wind
Breaks down as it is transported
How can we simulate transport?
Air-driven mill
Mars-analogue sand
For what purpose?
Characterize evolution over time
Survivability
Determine sources and pathways

## Slide 3: We created a mill to simulate Wind Transport
Mill configuration
Silicon carbide and epoxy body
Abrasion chamber
Glass plates
Mesh-covered air exit
Gaskets between mill and plates
Slotted air inlet
Experimental Setup
Airline secured to mill
Plates secured to body with clamps
Mounted for variable orientation
Notes: Assertion (title - question) – evidence (supporting text)
Transition from previous slide

## Slide 4: Our design evolved over time
Base Design1
Initial Design2
Final Design2
Image credit: 1Nitkiewicz and Sterner, 2Anna Baker
Notes: Assertion title (Our design evolved over time)
Image captions get lost – box/shaded something
Design evolution included testing a variety of gasket and panel materials, chamber volumes, air exit diameters, air inlet diameters and shape, and mill shape. All changes were made to reduce a source of error seen during testing.

## Slide 5: And in a number of ways
Inner chamber volume
Diameter of air inlet and exit holes
Gasket materials
Connections to airline
Shape of air inlet
Mill shape
Method of securing configuration
Front and back plate materials

## Slide 6: Building the Mill
Measure and mix epoxy-grit slurry
Deposit slurry into mold
Degas slurry using vacuum chamber
Remove mill from mold once dry
Sand front and back surfaces

## Slide 7: Testing the Mill

## Slide 8: Common Issues
Static buildup of grains on front plate
Non-circulating grains
Unstable setup
Broken plates

## Slide 9: Next Steps
Determine percentage of non-circulating grains
Run trials and analyze samples to determine best method and strength of circulation
Begin formal trials to characterize the evolution of Mars-analogue sand
Thank you: Devon Burr, Anna Baker, Paloma Rose Davidson, Arizona Space Grant Consortium, Northern Arizona University, Arizona State University, and NASA

## Slide 10: Technique progression
Tested various ratios of SiC-epoxy, technique for mixing and degassing slurry
Degassing technique:
Minimize air pockets
Uniform texture
Ratios: Texture
Maximum roughness while maintaining cohesion
Notes: Supplemental slide – testing ratios and methods