## Slide 1
Fin-induced Shock/Boundary Layer Interactions at Mach 5
Alec Maloney
Department of Aerospace and Mechanical Engineering
Space Grant Symposium, April 21-22 2023, Phoenix, AZ
Partner
Acknowledgments
Dr. Jesse Little, AME
Sathyan Padmanabhan, AME
Addison Plummer, AME
Notes: TFCL stands for Turbulence and Flow Control Laboratory.

## Slide 2: Introduction to SBLIs
Boeing
Thickening of the boundary layer and separation due to adverse pressure gradients
Increases heat transfer
Unsteadiness in the flow
Important for material life and control authority
Mears, Arora, Alvi. (2018)

## Slide 3: STORT Program
Boeing
Fin surface
Experiments to support DLR STORT Flight test data
Objective: Fundamental understanding of flow, unsteadiness, and heat flux of SBLI induced by double-sided fin
Gulhan et. al. (2022)
Threadgill et. al. (2022)

## Slide 4: Wind Tunnels
Boeing
Boeing
Fin surface
Mach 5 Ludweig Tube (LT5)
Mach 4.82 for 0.1 seconds
Large range of Reynolds numbers
Indraft Supersonic Wind tunnel (ISWT)
Mach 5.01 for up to 20 seconds
Threadgill et. al. (2022)
Notes: LT5: 4.8  849 m/s or 2785 ft/s
ISWT: 5.01 709 m/s or 2326 ft/s

## Slide 5: Oil Flow visualization
Visualizes important features such as the separation line
Conical shape does not change much with angle of attack
Padmanabhan et. al. (2023)
Notes: Virtual Conical Origin (VCO)

## Slide 6: Infrared Thermography
Boeing
Boeing
Fin surface
Reynolds Number
High
Low
Heating band due to reattachment
Reynolds number affects the structure and amount of heat transfer
Notes: Re is affecting the structure and heating of the SBLIs
Heating band due to reattachment

## Slide 7: Unsteady Pressure Measurements: ISWT
Boeing
Boeing
Fin surface
R1
S1
(Transitional)
Pressure transducers were used to measure pressure
Large amplification across lower frequencies
Notes: Power Spectral Density (PSD) graphs
Increased unsteadiness with higher power
Higher power means more energy of the pressure fluctuations

## Slide 8: Next Steps
Boeing
Boeing
Fin surface
Use heat flux sensors to get more data
Increase the length of the model to get data at higher Reynolds numbers
Compare our data to DLR flight test data
Threadgill et. al. (2022)

## Slide 9: Acknowledgements
Boeing
Boeing
Fin surface
Space Grant
My mentor Dr. Jesse Little
Everyone in the TFCL
Air Force Office of Scientific Research

## Slide 10
Thank You

## Slide 11: References
Boeing
Boeing
Fin surface
[1] Padmanabhan, S., Jouannais, L., Threadgill, J. et al. Laminar/Transitional Fin-induced Shock Wave Boundary-Layer Interactions at Mach 5.
[2] Threadgill, J., Jouannais, L., Hader, C. et al. Fin-induced Shock Boundary Layer Interactions on a Flat Plate and Hollow Cylinder at Mach 5.
[3] Plummer, A., Threadgill, J., Singh, A., Padmanabhan, S. & Little, J. (2023), 'Experimental Investigation of the STORT Flight Test at Mach 5,' AIAA Aviation Forum 2023, in preparation.
Notes: Missing Gulhan, A et. al. (2022) which is where the STORT images come from.