## Slide 1: Extraterrestrial Radiation's Impact on Ozone and its Implications for Climate and Health on a High-Altitude Ballooning Payload
Berkeley Adair, Elizabeth Garayzar, Muhammed Topiwala, Ricardo Ontiveros, Quang Huy Dinh, Alec Arcara, Joshua Sink, Tyler Nielsen
Notes: berkeley

## Slide 2: Goals
Design a thermally stable payload capable of measuring and recording atmospheric profiles
Safely house and retrieve footage from a 360 GoPro
Build a hybrid fiberglass & carbon fiber housing module
Design a universal PCB for future missions
Design and develop maintainable code for future missions
Science Mission #1: Radiation
Science Mission #2: Jet Stream
Notes: REMOVE

## Slide 3: UV vs Ionizing Radiation
Objective: Explore the link between cosmic/solar wind radiation, UVB radiation, and ozone layer dynamics
Approach: Simultaneous altitude-based measurements to analyze radiation-ozone correlations
Tools: UVB sensor + Geiger-Müller tube for cosmic/solar radiation
Notes: berkeley

## Slide 4: Jet Stream Dynamics
Objective: Analyze subtropical jet stream dynamics.
Approach: High-altitude, real-time atmospheric data collection.
Sensors
Wind: Linear air speed for current analysis (0-150MPH)
Temperature: Monitors jet stream temperature changes.
Humidity: Assesses moisture levels.
Gas/CO2: Evaluates atmospheric composition
Notes: berkeley

## Slide 5
Notes: berkeley

## Slide 6
System block diagram
Notes: jesse
Here is an overview of the electrical system
We are powered by an 11.1V battery.
Using 3.3V and 5V regulators.
Our payload’s brain is an Arduino RP2040 microcontroller that acts as our flight data recorder
Circuit is compatible with I2C, SPI, analog and digital inputs.

## Slide 7: Universal PCB
Logic Levels: Configurable 3.3V & 5V logic
Compatibility: Supports all Arduino Nano variants - Arduino RP2040
Connectivity: Plug-and-play with SPI, UART, I2C, Analog, and Digital inputs.
Power: External connectors for RAW, 5V, 3.3V; up to 3A output current.
Monitoring: INA260 IC for power monitoring
Control: L293D IC Motor Drive
Signal Processing: Custom RTD amplifier for precise temperature measurements.
Diagnostics: Built-in troubleshooting capabilities with embedded test points
Notes: jesse

## Slide 8
Flight Data Recorder Schematic
Notes: JESSE Point out that we included INA for power monitoring, motor driver for future missions, then using a diode PMOS combo for power protection

## Slide 9
PT1000 RTD Schematic
Notes: JESSE

## Slide 10: Onboard Sensors
PT1000
BME688
SHT30
LSM9DS1
ZOPT 2201 UVB
SGP30
Sparkfun M9N GPS
Modern Devices Wind Sensor
GoPro Max 360
Mighty Ohm Geiger Counter
Captures essential atmospheric data including wind speed, UVB, cosmic radiation, temperature, pressure, and humidity.
Notes: ELS
Purpose of Redundancy: Guarantees data reliability by counteracting sensor failure or inaccuracies
Array Configuration: Employs multiple sensors for recording identical measurements
Data Verification: Cross-reference outputs for accuracy, filtering out anomalies

## Slide 11: Onboard Sensors
SGP30
Sparkfun M9N GPS
Modern Devices Wind Sensor
GoPro Max 360
Mighty Ohm Geiger Counter
Purpose of Redundancy: Guarantees data reliability by counteracting sensor failure or inaccuracies
Array Configuration: Employs multiple sensors for recording identical measurements
Data Verification: Cross-reference outputs for accuracy, filtering out anomalies
Notes: Els
Can use notecard to read the redundancy, config, and verification infor stated in the slide

## Slide 12: Reliability through Sensor Redundancy
Purpose of Redundancy: Guarantees data reliability by counteracting sensor failure or inaccuracies
Array Configuration: Employs multiple sensors for recording identical measurements
Data Verification: Cross-reference outputs for accuracy, filtering out anomalies
Notes: REMOVE?

## Slide 13: Housing
Materials: 3K Honeycomb Carbon Fiber and Fiberglass Fabric.
External Components: Tough 2000 SLA Resin for sensor housing & mounting brackets.
Finish: XCR Clear Coating Resin topcoat for durability.
Fabrication Time: Estimated 16 hours per part. Using PLA mold
Notes: Huy

## Slide 14: Manufacturing Process
Step 1 : Preparation -Sanding and laminating the mold with PVC Mold Release Agent .
-Preparing the vacuum bag for the carbon fiber part , using Nylon Vacuum Bagging Film , Vacuum Seal Tape, and Air Valve.
Step 2 : Laminating
-Applying laminating resin and carbon fiber or fiberglass fibre to the molds . 3 layers of fibre is chosed as this provide good ratio between strength and weight.
Step 3 : Vacuum Bagging
-Put laminated mold into prepared vacuum bag and let part rest overnight.

## Slide 15: Stack
Framework: Secured with 4 M3 Threaded Rods.
Spacing: Custom-cut aluminum spacers for precise component alignment.
Camera Mount: Revised GoPro Max mount for enhanced payload destacking.
Notes: Josh

## Slide 16: Design Philosophy
More or less sensors? (scale)
Different kinds of sensors? (speed)
  Low- speed, High- speed?
What if we suffer temporary in- flight power disconnection issues? (data overwrite)
What if we suffer in- flight sensor disconnection issues? (single point of failure)
Software Design
Notes: Mo

## Slide 17: Software Overview
Implemented Object- Oriented paradigm to create a software framework to manage problems of scale and manage risk mitigation
Wrote clean, concise and maintainable code to open- source quality embedded software
Established a seamless system of version- control through Git and GitHub reducing time in code- sharing by 80%
Notes: Mo What if we suffer temporary in- flight power disconnection issues? (data overwrite)
What if we suffer in- flight sensor disconnection issues? (single point of failure)

## Slide 18: Software Overview
Object- Oriented paradigm
Modular and maintainable code
UML Design Diagram
Notes: Tyler Implemented Object- Oriented paradigm to create a software framework to manage problems of scale and manage risk mitigation
Wrote clean, concise and maintainable code to open- source quality embedded software
Established a seamless system of version- control through Git and GitHub reducing time in code- sharing by 80%

## Slide 19
Programming Tech Stack
Github hosts open source software development projects.
PlatformIO, a VS Code extension, provides the build system structure that automatically tags software dependencies and applies them using a modular hierarchy that takes away the usual complexity and pain.
Git is a distributed version control system that tracks changes in any set of computer files, usually used for coordinating work among programmers
Scan me to check out the Github repository 📲 🤳
Notes: Tyler Established a seamless system of version- control through Git and GitHub reducing time in code- sharing by 80%

## Slide 20: Testing: Thermal Chamber
Purpose: Validate the payload performance and resilience under extreme temperatures.
Conditions: Tests range from -50°C to +40°C to simulate high-altitude environments.
Key Takeaways
Ensure payload resilience to thermal stress.
Identify potential adjustments needed for mission readiness.
Difference of 15°C between external & internal temperatures - insulation functional
Notes: Alec

## Slide 21
Testing: Thermal Chamber
Notes: Alec

## Slide 22: Power Budget
Purpose: Ensure continuous operation and efficiency across all payload components during the mission
Scope: Covers all electrical systems including sensors, microcontroller, communication, and data storage
Source: 11.1V 3200 mAh LiPO Battery
Regulation and Distribution: LDO regulators stabilize voltages at desired 5V or 3.3V logic levels
Monitoring: INA260 IC monitors battery voltage (V), current draw (mA), and active power consumption (mW)
Notes: alec

## Slide 23
Testing: Power Budget
Notes: ALEC Shows the story of our power consumption - shows the spike when the camera is turned on

## Slide 24: Acknowledgements Dr. Tom Sharp Michelle Coe Desiree Crawl Sun Devil Satellite Lab Interplanetary Initiative ANSR
Questions?
Notes: Berkeley