## Slide 1: Flow Temperature Characterization of a Mach 5 Wind Tunnel
By: Veer Nayyar
Mentored by Dr. Alex Craig and Brian S. Kinsey
Boundary Layer Stability and Transition Laboratory
University of Arizona

## Slide 2: Background
Boundary Layer Transition
Mach 5 Ludwieg Tube (LT5)
Stagnation Temperature
  vs.
Bearden et. Al (2020)

## Slide 3: Objectives
Design, manufacture, and test a purpose-built total temperature probe
Gather reliable temperature measurements to inform future research
Identify LT5 operating parameters
Buttsworth, Widodo (2010)
Wood (1959)

## Slide 4: Probe Design
Ahmic Thin-Film platinum resistance thermometer (PRT)
Rigid 10K casings
Stainless steel housing
Nichrome alloy heating wire

## Slide 5: Mounting Hardware
1” radius adjustable clamps
  8 counterbored, threaded slots
  Can be mounted in tandem with experimental models
Extended wedge
  3.8” vertical projection
  Wire routing, probe mounting

## Slide 6: Wind Tunnel Testing
4 tests completed
Identical initial signal response due to isentropic expansion
Total temperature measured within 0.15 seconds after tunnel fires

## Slide 7: Wind Tunnel Testing
Preheats near total temperature reduce overall signal response amplitude
Signal behavior deviates during flow stagnation
Narrows search window for future total temperature measurements

## Slide 8: Conclusions and Future Research
Developed and tested purpose-built measurement hardware
Determined specific search criterion for future experiments
Redesign probe to house thermocouples
Develop flow temperature profile with multi-point measurement hardware
Understand discrepancies between measured total temperature and numerical models
Arnold Air Force Base

## Slide 9: Acknowledgements
NASA Arizona Space Grant Consortium
Dr. Alex Craig and Brian Kinsey
BLST colleagues and fellow space grant interns

## Slide 10: Thank You