## Slide 1: ERAU ASCEND! STRUCTURES and SYSTEMS INTEGRATION
Nicholas Hammons

## Slide 2: PREVIOUS STRUCTURE
Fold-out poster board mounting
Carbon fiber-epoxy lid
  External GPS
Velcro mounting
Inseparable subsystems
Wiring mess

## Slide 3: GOALS
Improve component accessibility
Separate subsystems
Reduce wiring mess
Internalize GPS antenna
Integrate PICAXE microcontroller
Add solar cell module
Lighten payload (< 4 lbs)

## Slide 4: SOLUTIONS
Accessibility: Slide-out flanges
Sys. Separation: Separate power systems
Separate levels
Wiring: Ribbon cable/connectors
GPS: Glass-epoxy lid
PICAXE: Data board
Solar Cells: Lid-mounted module
Weight: Composites

## Slide 5: CURRENT PAYLOAD STUCTURE
Shell
Lid
Shelving System
  APRS Layer
  Data Collection Layer

## Slide 6: PAYLOAD SHELL
Inherited/reusable shell
  5 launches
8” x 8” x 8” cube
Bi-directional carbon fiber
¼” foam core
External access to on/off switches
~ 421 in3 useable volume

## Slide 7: PAYLOAD LID
Glass-epoxy
  GPS transmission
¼” foam core
GPS antenna/ground plane mounted internally
Solar cells mounting
Silicon gel to reduce heat flux

## Slide 8: SOLAR CELL MODULE
Glass-epoxy
¼” foam core
Plexiglas cover

## Slide 9: SHELVING SYSTEM
Mimic EYASSAT NanoSat Modules
Separate power requirements
Carbon fiber-epoxy laminate
  Slide-out flanges: 3-ply
  Brackets: 2-ply
Reduces structure volume and weight
  ~ 7.5% more internal volume
  (vs. Nov. 22, 2008 launch)

## Slide 10: APRS LAYER
TinyTrak 4
Radio
GPS Evaluation Board
Voltage Regulator
AA Battery Pack

## Slide 11: DATA COLLECTION LAYER
¼” foam core
Data board:
  PICAXE
  Logomatic
  Voltage Regulator
  Internal/External Temperature Sensors
  Pressure Sensor
AA Battery Pack

## Slide 12: SYSTEM INTEGRATION
Velcro mounting
1 cross-board connection
  On/off switch
2 lid to payload connections
  Solar cells
  GPS antenna
External on/off switches
Payload weight at launch:
  3 lbs 11 oz

## Slide 13: FUTURE IMPROVEMENTS
Integrate data collection system into PC boards
  Convertible payload
  Reduce APRS volume to maximize space for collecting data
Fabricate sun sensor module
Improve thermal regulation

## Slide 14: QUESTIONS

## Slide 15: ATTITUDE DETERMINATION
Andrew Grant