## Slide 1: Embry-Riddle Aeronautical University ASCEND! Project Overview
By: Geimi DeLarge
NASA Space Grant – ASCEND!
Mentors: Dr. Ronald Madler, Jack Crabtree
April 17, 2010

## Slide 2: Overview
The Team
Flight Objectives
Payload Components
Data Acquisition
The Launches
Conclusion

## Slide 3: The Team
4/17/2010
Noah Stokely, Jessica Avitia, Mary Begay, Geimi DeLarge, and Nicholas Hammons

## Slide 4: Flight Objectives
Gather atmospheric data
Experiment with composite structures and construction methods
Gather pressure data
Gather Geiger counter data
Gather sunsensor data
4/17/2010

## Slide 5: Payload Components
Pressure Sensor
SD Datalogger
Internal Temperature

## Slide 6: Payload Components
Source: www.embeddeddatasystems.com
Source: http://rocky.digikey.com
Dallas DS18B20 – One Wire Device
Digital Sensor
Internal/External
9 – 12 bit Measurements
Degrees Celsius
Range of -55°C to +125°C
Accurate to ±0.5°C
Honywell Analog Pressure Sensor – ASDX Series
Analog Sensor
Approx. Frequency : 1Hz
Range: 0 – 15 psi
Absolute Pressure

## Slide 7: Payload Components
Source: imagesco.com
Digital Geiger Counter
Alpha, Beta, and Gamma rays
Compare to altitude

## Slide 8: Payload Components
  Sun Sensor:
    Fall 2009
  3 solar cells mounted on exterior of payload
  Record Voltage
  Compare with altitude
  Check for viability for future sun sensor
    Spring 2010
    Photoresistors took the place of the solar cells
Spring 2010: Payload Lid

## Slide 9: Data Acquisition System
Source: www.hvwtech.com
Source: www.inmotion.pt
UK-based microcontroller system
Basic Programming Language
28-X1 Chip
Faster Serial Output Capabilities
Larger Memory
Converts Analog Signal
  8 bit
  10 bit
Logomatic Data Logger
  Utilizes SD Card – Up to 2GB
  FAT16 Format
  Serial Input From Picaxe

## Slide 10: Fall 2009 Launch
Max altitude: 84,803 feet
Distance traveled: 72.53 miles
Components Flown:
  Temperature
  Pressure
  Geiger Counter
  Solar Cells
  GPS

## Slide 11: Spring 2010 Launch
Max altitude: 84,803 feet
Flight distance:89.85 miles
Components Flown:
  Temperature
  Pressure
  Geiger Counter
  Photoresistor

## Slide 12: Conclusion
Two successful flights for the 2009-2010 academic year
Hopefully use data to aid in the development of a sun sensor
Continue ASCENDing!

## Slide 13: QUESTIONS??