## Slide 1: Carbon Dioxide Emissions Implications if Hydrofluorocarbons are Regulated
A Comparison of Refrigerants
James Lownsbury
E
C
inside freezer
T= -17 oC
36 oC
heat ejection medium
-23 oC
Thot
ambient air
T = 47 oC

## Slide 2: HFC Regulation
The EPA announced last year that HFCs, CO2, and other greenhouse gases are hazardous to human health because of their roles in global climate change.
Like CFCs before them, HFCs are likely to be regulated due to their adverse affects on the environment.
HFEs (hydrofluoroethers) are likely candidates to replace HFCs in a variety of applications, including refrigeration.

## Slide 3: How does refrigeration work?
Thot
Compressor
Cond.
Valve
Evap.
1
2
3
4
By law: Tfreezer = -17 oC
Worst-case:
Tair = 47 oC
Qfan
Freezer temperature sets the maximum refrigerant temperature T1 = -23 oC P1 > 1 atm Liquid-vapor mixture
Ambient water Twater = 25 oC
Minimum ΔT = 11 oC T4 = 36 oC Must be all liquid Vapor pressure data + T4  P4
No pressure drop through heat exchangers
P3 = P4
P2 = P1
By law: Tdischarge < 48.9 oC

## Slide 4: Some equations used
Major sources of indirect CO2 emissions.
Compressor
Cond.
Valve
Evap.
1
2
3
4
Tfreezer = -17 oC
Qfan
Ambient water Twater = 25 oC
P3 = P4
P2 = P1
Tdischarge < 48.9 oC
Antoine Equation:
T4 = 36 oC
 ideal T3 
Tair = 47 oC
Cp values for the HFE from: P. Blowers, K. F. Tetrault, Y. Trujillo-Morehead, Estimation of heat capacities for hydrofluoroethers with two carbon atoms, Ind. Engr. Chem. Res., 46, 6600-6604, (2007).

## Slide 5: Global Warming Effects
Indirect CO2 emissions:
    1.05 kg CO2 per kWh of electricity from coal
    0.003 kg CO2 per L of water pumped
Direct CO2 equivalent emissions:
  9% leakage per year
    R-12 (CFC): GWP = 8100
    R-134a (HFC): GWP = 1300
    HFE-143m: GWP = 446
P. Blowers and J. Lownsbury, Carbon dioxide emission implications if hydrofluorocarbons are regulated: A refrigeration case study, Env. Sci. Technol., 44, 1526-1529 (2010).

## Slide 6: Comparison of Results
Refrigerant | R-12 | R-134a | HFE-143m
Ws,compressor [J s-1] | 19,545 | 29,259 | 33,956
mwater [g s-1] | 625 | 802 | 897
Comp. electricity [kWh y-1] | 171,214 | 256,309 | 297,455
Water movement [kWh y-1] | 59,130 | 75,895 | 84,879
Electricity losses [kWh y-1] | 17,872 | 25,775 | 29,664
Direct CO2-eq. emissions | 97,920 | 21,456 | 6,966
Indirect CO2 emissions | 260,627 | 357,877 | 432,597
Total CO2 emissions | 358,547 | 397,933 | 439,563
Good!
Bad!
From a global warming perspective, the most attractive refrigerant would be the CFC, but since CFCs are ozone depletors, the HFC would be the best choice.

## Slide 7: Sensitivity analyses
The solid line - current HFC (R-134a), the dashed line - phased out CFC (R-12), and the dash-dot line - likely HFE replacement (CF3OCH3). Indirect and direct emissions total in 105 kg/year.
P. Blowers and J. Lownsbury, Carbon dioxide emission implications if hydrofluorocarbons are regulated: A refrigeration case study, Env. Sci. Technol., 44, 1526-1529 (2010).

## Slide 8: Up next…
HFEs in window AC units
HFEs in car AC units
HFEs in dry cleaning applications
Questions?