## Slide 1: Fabrication Methods and Materials for Dielectric Barrier Discharge Plasma Actuators
Marianna Yanes
Mentor: Jesse Little, Assistant Professor in the Aerospace and Mechanical Engineering Department
21st Annual Arizona Space Grant Consortium Symposium
University of Arizona
April 21, 2012

## Slide 2: Dielectric Barrier Discharge (DBD)Plasma Actuators
DBD plasma actuators are constructed using two electrodes separated by an insulating dielectric barrier.
When a high voltage (10-30 kV) waveform (AC or nanosecond pulse) is provided between electrodes, an electrical discharge (plasma) is formed.
This ionized air (plasma) can transfer momentum to the neutral air and can also generate shock waves.
This can have beneficial effects in many applications, but our focus is aerodynamics.

## Slide 3: Plasma discharge
Pictures and movie from: Jesse Little

## Slide 4: Actuator Performance
High angle of attack on airplane flow separation high drag and low lift.
Efficiency goes down  Safety problems.
Plasma actuators on wings prevent flow separation decreasing drag and increasing lift.
If flow separation is prevented, airplanes can fly at higher angles of attack.
Movie from: Jesse Little

## Slide 5: What’s so special about DBD plasma actuators?
Light and simple to construct
Surface mounted with no moving parts
Minimally affect the wing when not in use  no change in aerodynamic shape.
Closed loop feedback control for smooth variations of forcing frequency and power in dynamic flight environments
There is debate on the physics underlying of these devices and their effect on the airflow

## Slide 6: Impact UV Method will have
Research comes in because:
The actuator must be accurately and repeatedly constructed to allow investigation of the physics.
Studies show that:
3D designs provide a 3-D forcing mechanism that combines effects of different type of actuators.
Provide x, y, and z momentum or shock waves to the fluid.
Future studies:
Using different actuator designs is useful for uncovering unknown airflow mechanisms.
Could lead to novel, more efficient aircraft design notions.

## Slide 7: Construction Methods
Figure template
Design template
Cutting with exacto knife
Tedious
Prone to deficiencies
Would be challenging for constructing 3D models.
UV photoresist
Used for printed circuit boards (PCBs)
Exposes photosensitive film with artwork to UV light and transfers pattern to board.
Exacto knife
Copper/ Kapton tape
Easiest method
Stacking metal and insulating tape

## Slide 8: Ultraviolet (UV) Photoresist Method
UV exposure system
Transparencies with artwork
Photosensitive
film
Copper clad board
Abrasive pad
Scissors
Timer
Hair dryer

## Slide 9: Development Process
Safe light environment
Safety equipment
Negative developer
Developing tray
Etching tray
+
Measuring cup

## Slide 10
Results
Provides better quality and more repeatable actuators.
Allows for easy construction of different electrode patterns (3D).
Finger actuator
2D actuator
Bottom electrode
Top electrode
Top electrode
Bottom electrode

## Slide 11
Plasma Formation
Light on
Light off
Plasma
Tested actuator
Frequency: 3kHz, nanosecond pulse ~12 kV

## Slide 12: Special Thanks
NASA for granting me the opportunity.
U of A for your wonderful research and NASA affiliation.
Dr. Little, my mentor, for being an outstanding boss and instructor.
Associated Space Grant staff: Susan Brew, Tara Brode, Karis.
Dimuth, my advisor.
Shelley for keeping me updated.
Refer to uanews.org for more stories and slideshows.

## Slide 13: Our plasma actuators
~ ½ mm thickness
Can fit perfectly on the surface of an airfoil
Low power (AC and nanosecond pulsed)
Nanosecond use less power than AC actuators
High amplitude and bandwidth potential
NS-DBDs = results are better in high velocities.
AC-DBDs = good results in lower velocities.

## Slide 14: Dielectric and plasma
Dielectric= electrical insulator. Can be polarized by an applied electric field.
Unlike a conductor, electric charges do not easily flow.
Dielectric polarization=positive charges are displaced toward the field and negative charges shift in the opposite direction.
Plasma= gas atoms are excited to higher energy states and also ionized.
Relaxation of atoms to lower energy states release of photon of light glow discharge with color