## Slide 1
UAV Wing Design For Efficiency At Low Reynolds Numbers
Presented by Devin Jensen
Embry-Riddle Aeronautical University

## Slide 2
Wing Design
2D optimization
3D optimization
Control
Lessons Learned
Overview

## Slide 3
2D Optimization
Airfoil chosen from Selig and Eppler airfoils
Sellig 4110 chosen
High Cl/Cd
Acceptable pitching moment
Wing Design

## Slide 4
3D Optimization
Estimated weight of 8 lbs.
Wanted 10 lbs. of lift
Analyzed a series of wing geometries
Calculated lift and drag
Wing Design

## Slide 5
Wing Design
3D Optimization
Continued
Wing geometry description for chosen wing
Aspect Ratio = 6
Taper Ratio = 0.5
C/4 sweep = 0
Planform Area = 7.5 square feet

## Slide 6
Control
20 percent of wing area for horizontal tail
10 percent of wing area for horizontal tail
Ailerons, rudder and elevator used for control
Wing Design

## Slide 7
Lessons Learned
V-Tail
Flaps
Greater tail area
More dihedral
Pod attachment
Addition of incidence angle
Wing Design

## Slide 8
Questions?