## Slide 1: Greenhouse Gas Emissions for Refrigerant Choices in Room Air Conditioner Units
Michael Galka and Dr. Paul Blowers
The University of Arizona
NASA Space Grant Internship Program
Fall 2011-Spring 2012

## Slide 2: Introduction-Room Air Conditioners
Air conditioner
  Compressor
  Condenser
  Evaporator
  Expansion Valve
  2 fans
2 tons (24,000 Btu) cooling

## Slide 3: RACs in the U.S.
AC ownership information from EIA in 2009
25.9 million homes with at least 1 RAC unit
Total comes to 23% of all U.S. households have at least one RAC
RAC ownership and use is likely to increase as the standards of living rise worldwide
Notes: Reasons for likely increase in use of RACs is low cost of production and easy transport. Also have lower values of electricity consumption than central air conditioning which favor areas where strong electrical grids are not established.

## Slide 4: History of Refrigerants
Some of the first refrigerants included
  Ammonia (toxic)
  HCs such as propane (flammable)
CFCs synthesized in 1930s
  Replaced use of HCs
  R-12 (ODP=1, GWP=10900)
  Montreal Protocol banned production (1987)
HCFCs synthesized in 1980s
  Replacing CFCs
  R-22 (ODP=0.06, GWP=1810)
  Montreal Protocol banned production (1992)

## Slide 5: Today’s Refrigerant
HFCs synthesized as replacement for HCFCs
  R-134a
  Commonly used in air conditioners
  ODP=0, GWP=1600
  Emissions continually increasing since 1990
  Little regulation by Clean Air Act

## Slide 7: Possible Refrigerant of the Future
Hydrofluoroethers (HFE)
  Not regulated due to low GWP and atmospheric lifetime
  Increased patents issued for various applications in recent years
  Similar properties to current refrigerants in refrigeration
  If HFCs fall subject to regulation HFEs could be next in line to replace them

## Slide 8: Some Refrigerants Tested
  Ammonia (NH3)
  Propane (C3H8)
  Dimethyl Ether (CH3OCH3)
  R-22 (CHClF2 )
  R-134a (C2H2F4)
  HFE-152a (CF2 HOCH3)
  HFE-143m (CF3OCH3)
  Total of 18 refrigerants examined in the study.

## Slide 9: Vapor Compression Refrigeration Cycle

## Slide 10: Calculating Results
Model in Excel
Visual basic programming
First and Second Laws of Thermodynamics
Energy and Heat Balances
Sensitivity Analysis

## Slide 11: Resulting Numbers of Emissions
R-22 (Standard)
  1,160 kg CO2-equivalent / year per unit
  30.03 metric tons CO2-equivalent / year in U.S.
HFE-143m
  1,260 kg CO2-equivalent / year per unit
  32.62 metric tons CO2-equivalent / year in U.S.
NH3 (Ammonia)
  1,070 kg CO2-equivalent / year per unit
  27.72 metric tons CO2-equivalent / year in U.S.

## Slide 12: Trends and Sensitivity Analysis
Emissions increase as ambient temperature increases.
Emissions increase at thermostat temperature settings decrease.
As refrigerant emissions during disposal of equipment increase R-22, R-134a, and HFE-143m are undesirable.
Improving compressor and line transmission efficiencies decrease emissions using all refrigerants.

## Slide 13: Sensitivity analysis

## Slide 14: Conclusion of Study
Dimethyl ether, ammonia, propane, R-152a, and HFE-152a produce lower emissions than currently used refrigerants R-22 and R-134a.
HFE-143m produces nearly identical emissions as R-22
More emissions stem from warmer climates and lower thermostat settings.
Notes: -Although flammable and/or toxic dimethyl ether, ammonia, and propane should be considered as legitimate substitutes for currently used HFCs due to the very small leakage rates of RAC units.

## Slide 15: Additional Considerations
Others to be considered are:
  New refrigerants being created in industry
  Policies regarding air conditioning settings in southwest U.S.
  Other more sustainable energy sources to meet high electricity needs of U.S.
  Environmental impact of recovery and reclamation processes for refrigerants

## Slide 16: Acknowledgments
NASA Space Grant Internship Program
Paul Blowers, PhD

## Slide 17: Questions???
Michael Galka
mgalka@email.arizona.edu