## Slide 1: In-Situ Butanol Recovery from Fermentations via Expanded-Bed Adsorption
Michael Wiehn
Dr. David Nielsen
2012 NASA Space Grant Symposium
University of Arizona
April 21, 2012

## Slide 2: Motivation
Global crude oil depleted in 40 years
Replace gasoline with bio-butanol
n-Butanol can be burned in automobile engines
Enthalpy of Combustion:
  Gasoline – 44.40 MJ/kg
  n-Butanol – 33.08 MJ/kg

## Slide 3: Biobutanol
Clostridium acetobutylicum
  Rod-like shape, anaerobic, soil bacteria
  Glucose fermentation into butanol, acetone, and ethanol – 6:3:1 ratio
  Wild-type butanol production rate of 0.37 g/L·hr
Butanol is lethal above 10 g/L

## Slide 4: Adsorption
Hydrophobic polymer resins
  0.30-0.84 mm in size
  Over 1,100 m2 surface area per gram
Butanol
  Hydrophobic carbon chain
  Hydrophilic alcohol group

## Slide 5: Process Flow Diagram

## Slide 6: Results
Chart: Time (min)
| 0 | 1 | 3 | 5 | 10 | 15 | 20 | 25 | 30 | 40 | 50 | 60 | 80 | 100 | 120 | 150 | 180
40.083 g wet resin | 14.1749 | 13.5051 | 12.5943 | 12.1914 | 11.5041 | 11.2624 | 11.0088 | 10.9772 | 11.1471 | 11.0128 | 10.8501 | 10.4907 | 10.7487 | 10.8743 | 10.8045 | 10.8324 | 10.872
80.030 g wet resin | 13.634 | 13.5727 | 12.2454 | 11.732 | 10.434 | 9.6109 | 9.3941 | 9.4105 | 9.3233 | 9.38 | 9.5845 | 9.4938 | 9.5054 | 9.4465 | 9.5043 | 9.4251 | 9.3636
119.992 g wet resin | 14.1908 | 13.0999 | 12.0473 | 11.8926 | 10.082 | 9.2431 | 8.563 | 8.3513 | 8.4148 | 8.2691 | 8.215 | 8.241 | 8.1192 | 7.9461 | 8.059 | 7.8926 | 8.1414
40 g wet resin
80 g wet resin
120 g wet resin

## Slide 7: Conclusions
Butanol is a viable option for gasoline replacement as a liquid transportation fuel
Expanded-bed adsorption system can avoid the toxicity ceiling in fermentations
Adsorbents are the most promising method of separation
Future work will entail active bacteria cultures

## Slide 8: Thank you! Questions?