## Slide 1
Advisor: Prof. Jesse Little
Modification of a High-Speed Jet for Study of Active Flow Control
Department of Aerospace and Mechanical Engineering
Nicolas Urias
Arizona Space Grant Consortium Symposium
April 12th, 2014
Tucson, AZ

## Slide 2: Introduction
High speed jet located inside anechoic chamber
Operated by high pressure tanks
  Initial pressure of 1750 psi
  System drops pressure to 300 psi in settling chamber
Lucas 2011

## Slide 3: Active Flow Control Background
Control of turbulent jet structures
Actuators are installed along the inside wall of diffuser
  Allows some control of where the fluid attaches to wall of diffuser
    Thrust Vectoring in aircraft/spacecraft
Pack and Seifert 2001

## Slide 4: Circle to Square Transition Block
Designed to fit existing jet facility
  Converts circular flow to simplified 2D flow
    Simpler to install actuators
Had to match existing internal jet nozzle exit angle
  Required many measurements

## Slide 5: Circle to Square Transition Block
Square had to fit inside circle to be machinable
Designed using SolidWorks to obtain high machined precision
Contours of the part could NOT be produced with traditional machining tools
  Outsourced machining work to specialists
Notes: How about mentioning some of the design criteria (pressure, area change, length, etc.).

## Slide 6: Circle to Square Transition Block
Part could only be wire electric discharged machined (Wire EDM).
  High tolerances could be achieved (ten thousandth of an inch)
  Required clearance for wire inside part
Part was to be made of Stainless Steel
  Very durable and “easily” machined
  Could handle the weight of all other flow control components attached to the downstream end

## Slide 7: Wire EDM

## Slide 8: Illustration of Contours

## Slide 9: Issues with Design
Wire EDM machinist could not get exact contours of adapter block
SolidWorks Education Edition not suitable for high-quality .DXF exportation
  Virtually no way to program wire EDM machine to produce the exact part required

## Slide 10: Issues with Design
Dramatized contour showing discontinuity

## Slide 11: Test Apparatus Setup
A flat plate mounts to C-S transition block
2D diffuser mounts to the flat plate
Actuators inserted into diffuser cone
  Can achieve thrust vectoring and noise reduction in nozzle exhausts

## Slide 12: Test Apparatus Setup
Inlet
Flat plate
Diffuser cone
Actuator location
Outlet

## Slide 13: Test Apparatus Setup

## Slide 14: Future Tasks
Finding a solution for the SolidWorks to .DXF conversion issue
  Use NX Nastran software
    Designed for aerospace companies
Design internal cavities for actuators
Design diffuser cone

## Slide 15: Thank you!!
The NASA Space Grant
The A.F.S.O.R.
&
Special thanks Dr. Lutz Taubert, whom helped me with every aspect of this design project.

## Slide 16: References
Pack, Latunia G., and Avi Seifert. "Periodic Excitation for Jet Vectoring and Enhanced Spreading." Journal of Aircraft 38.3 (2001): 486-95. Print.
Lucas, Nathaniel. IMPROVING FLOW RATE CONTROL FOR A SUPERSONIC TWIN NOZZLE AND REDUCING NOISE WITH FLEXIBLE FILAMENTS. Thesis. University of Arizona, 2011. N.p.: n.p., n.d. Print.